## Slide 1: An Introduction to Wireless Time Sensitive Networking
Presenter: Javier Perez-Ramirez
Contributors (in alphabetical order): Dave Cavalcanti, Carlos Cordeiro, Dibakar Das, Fatemeh Fazel, Minyoung Park and Ganesh Venkatesan
March 2022

## Slide 2: Presentation Overview
An Introduction to Wi-Fi
What is Wireless Time Sensitive Networking (WTSN)?
Recent Results and Demos
WTSN Use Case for XR
Concluding Remarks

## Slide 3: An Introduction to Wi-Fi

## Slide 4: Current Generations of Wi-Fi
Wi-Fi 5
Wi-Fi 6/6E
Wi-Fi 4
Wi-Fi 6E
  Extends Wi-Fi 6 with 6 GHz band operation*
  Launched Jan’2021
Based on IEEE 802.11ax
2.4, 5, 6 GHz band operation
OFDMA, UL and DL MU-MIMO, target wake time (TWT), 1024-QAM
Best-in-class WPA3 security
Max data rate: 9.6 Gbps
Launched Aug/2019
Based on IEEE 802.11ac
5 GHz band operation
Up to 8x8 MIMO, DL MU-MIMO, 80 MHz and 160 MHz channels, 256-QAM
Max data rate: ~7 Gbps
Launched June/2013
Based on IEEE 802.11n
2.4 and 5 GHz band operation
Up to 4x4 MIMO, 40 MHz channels, 64-QAM
Max data rate: ~600 Mbps
Launched in 2007
Source: https://www.intel.com/content/dam/www/public/us/en/documents/pdf/wi-fi-7-and-beyond.pdf
* Availability depending on regulatory domain

## Slide 5: Improvement with 802.11ax trigger-based (OFDMA) access
  OFDMA reduces latency by avoiding multi-user contentions
  Scheduled access allows better control of channel access and link adaptation
≈1300 µs
≈ 758 µs
Notes: Instead of relying application level scheduling..its possible to do schedule at the MAC and lower layers..which gives much more control and determinism

## Slide 6: 802.11ax with optimized scheduling (simulations)
PDR: Packet Delivery Ratio (Fraction of packets successfully delivered within the latency bound)
Simulation Assumptions:
20 MHz channel, SISO, 100 Bytes packets, Channel model E, STAs randomly distributed in a 50 m radio, latency-optimized scheduling strategy, managed network (no OBSS), no legacy devices.
Chart: Capacity vs. Latency bound (msec) for Target PDR = 99.999%
| 1 | 1.5 | 2 | 2.5 | 3
Capacity | 9 | 18 | 28 | 35 | 45
Low latency/high reliability and capacity tradeoffs can be achieved

## Slide 7: Wi-Fi 6 on 6GHz band (Wi-Fi 6E)
Huge contiguous clean spectrum
    Up to 1200 MHz, many more (wider) channels
    Ideal for deterministic, low latency operation in managed/controlled networks
802.11-based products must implement the 802.11ax specification to operate in 6 GHz band
    No legacy (pre-802.11ax) devices
 |  | 2.4GHz Band | 5GHz Band | 6GHz Band
Spectrum |  | 85MHz | 480MHz | 1200MHz
20MHz Channels |  | 3 | 25 | 59
40MHz Channels |  | 1 | 12 | 29
80MHz Channels |  | 0 | 6 | 14
160MHz Channels |  | 0 | 2 | 7

## Slide 8: Wi-Fi 7 Key Features – Data Rate

## Slide 9: Wi-Fi 7 Key Features - MLO

## Slide 10: Deterministic Wi-Fi
Wireless TSN
Time synch (.1AS)
Time-aware scheduling (.1Qbv)
Redundancy (.1CB)
Network
E2E wireless-wired integration Management & scheduling
Enablers
6 GHz Multi-radio clients/ APs
Core Capabilities
QoS management
802.11ax: OFDMA, Triggered access
802.11be MLO,320 MHz, Restricted TWT
Deterministic Wi-Fi Enabling Tools

## Slide 11: What is WTSN?

## Slide 12: TSN
Time-Sensitive Networking (TSN) = deterministic data delivery with bounded latency without loss due to congestion or errors
Standards defined by the IEEE 802.1 TSN Task Group for IEEE 802 Local Area Networks (LAN)
TSN Translation
5G
System
802.3 (Ethernet)
802.11
(Wi-Fi)
TSN Tools
IEEE 802
LANs
TSN enhances standard connectivity (Ethernet, Wi-Fi, and 5G)
Notes: TSN is about deterministic data delivery without loss
TSN is enabled by a set of tools, mainly networking protocols in four main areas (sync, latency, reliability and resource management) and HW/SW optimizations to achieve time-synchronized deterministic communications
IEEE based TSN and integration with non-IEEE (5G)

## Slide 13: Examples: accurate time and data delivered within deadlines are critical
Isochronous Industrial Control
Sensing
Actuation
Control
Sensor fusion: multi-camera time synchronized with low latency & jitter
Extended Reality: user input, computing and display with low latency
Source: Microsoft Mesh
HMD
Computing
“Sensing”
“Actuation”

## Slide 14: Time Synchronization (802.1AS) & Time-Aware Shaping (802.1Qbv) over Wi-Fi
802.1AS synchronization across wired-wireless TSN
  802.11 defined MAC specific support for 802.1AS:
    Timing Measurement (TM) – IEEE802.11-2012
    Fine Timing Measurement (FTM) – IEEE802.11-2016
Talker
Listener
STA 1
T
T
T
T
T
T
T
T
T
T
T
T
Shared medium
STA 2
Queues/Traffic Classes
AP
802.1Qbv time-aware scheduling in WiFi
  A time-aware (Qbv) scheduler defines when gates open/close to ensure time-sensitive frames are not delayed by other traffic

## Slide 15
Time Synchronization – 802.1AS over 802.11 TM/FTM
802.11 action frames are used to compute:
LinkDelay = [(t4-t1)-(t3-t2)]/2
  NeighborRateRatio* = (t1’-t1)/(t2’-t2)
  TimeOffset = [(t2-t1)-(t4-t3)]/2
STA
AP (Soft-AP)
 | Accuracy
90% | +/-2.8us
75% | +/- 2.5 us
50% | +/- 1.8 us ns
25% | +/- 750 ns
12.50% | +/- 260 ns

## Slide 16
Time Aware Traffic Shaping – 802.1Qbv over 802.11
Example Schedule
Latency distribution without Qbv schedules
Latency distribution with Qbv schedules
Test Setup for Qbv over 802.11ac/Wi-Fi 5
AP
Talker
Client
Listener
DUTs

## Slide 17: Recent Results and Demos

## Slide 18
Accurate Time Synchronization + Time Aware Traffic Shaping – Demo
WTSN Vision-based Robot Grasping
Soft-griper for pick and place tasks over Wireless Time Sensitive Network in collaboration with ISR/Human Robot Collaboration group.

## Slide 19: Industrial Control Demo @ MWC’22
https://youtu.be/PYoYrc7h-iA

## Slide 20: WTSN Use Case for XR

## Slide 21: Motivation
How can we enable high quality xr experiences with a lightweight headset form factor?

## Slide 22: Motivation
remote rendering
How can we enable high quality xr experiences with a lightweight headset form factor?
+

## Slide 23: Motivation
remote rendering use cases
edge
…
Next gen
Current off-the-shelf Wi-Fi does not meet requirements of XR experiences.
INTEL is interested in understanding complete top to bottom XR technologies to identify gaps in current wireless connectivity solutions (e.g., Wi-Fi).
Next gen

## Slide 24: Collaboration with ILLIXR Team
Integrate WTSN SW Stack in ILLIXR.
Offload ILLIXR module(s) to client device (e.g., laptop) and evaluate QoE performance.

## Slide 25: Concluding Remarks

## Slide 26
Concluding Remarks
Next generation Wi-Fi will offer more deterministic, latency bounded communications.
WTSN technologies allow for single digit wireless time synchronization accuracy with deterministic latency.
XR experiences can leverage these new features to improve QoE offloading compute to client/edge/cloud.
  Need to understand application requirements/behavior.
  Use this knowledge to configure TSN features.
  Identify Wi-Fi gaps and opportunities for optimization.
We are planning to integrate WTSN in ILLIXR testbed to evaluate impact of QoE when offloading HMD modules to client device.

## Slide 28: 802.11ax Tx latency analysis
PPDU* tx times as a function of RU size and MCS
  Once channel is acquired, latency can be very low
  for typical 1500bytes packets depending on bandwidth and channel/MCS
  for small packets (e.g.,100 bytes), low latency can be achieved with smaller RU sizes if channel condition is good enough
  802.11ax enables latency vs. reliability tradeoffs
*PPDU = Physical layer Protocol Data Unit