## Slide 1: Physics 101 - Lecture 23
Today’s lecture will cover sections 13.1 to 13.5
1

## Slide 2
2
What is temperature?
Bimetallic Strip
Physical Sensation
  Hotness or Coldness
  Not very useful
Zeroth Law of Thermodynamics
  Thermometric properties
    Intermolecular spacing standard thermometer
    Electrical resistance thermistor
    Fermi level thermocouple
  Temperature Scales
    Fahrenheit
    Celsius
    Kelvin
    Rankin

## Slide 3
3
Modeling Thermal Expansion
Change in length is proportional to change in temperature.
  Coefficient of linear expansion can be modeled at the molecular level but we look it up in a table.
  ∆T is measured relative to the temperature at which L0 is measured.
  Volume scales as (length)3 so β = 3α and
Clicker Question (L23Q1): Suppose that a temperature increase of 30°C increases the length of a 2.0000m long bar of metal by 3.5mm. What is the coefficient of thermal expansion for this metal?
A) 5.83·10-5/°C
B) 1.17·10-1/°C
C) 1.75·10-3/°C
D) 6.67·10-2/°C

## Slide 4
4
Example: Locomotive Tire
Ball and loop
A cast iron wheel ( αCI = 10.4·10-6/°C ) is to be fitted with a 304 austenitic stainless steel tire ( αSS = 17.3·10-6/°C ). At the standard temperature of 20°C, the inner diameter of the tire is 2.0000m while the outer diameter of the wheel is made to be 2.0020m. To what temperature must the pair be heated if they are to just slide together?
Main idea: The two diameters must be made to match. This will happen at some elevated temperature.
Solve for ∆T.

## Slide 5
5
Historical View of the Ideal Gas Equation of State
Set of four experiments leads to a description of dilute gasses.
  Robert Boyle ( 1662 ) Constant Temperature, Mass
  Jacques Charles ( 1780’s ) Constant Pressure, Mass
  Joseph Gay-Lussac ( 1809 ) Constant Volume, Mass
  Lorenzo Avogadro ( 1811 ) Constant Temperature, Pressure
Cylinder of volume V, filled with some mass of gas, m.
Piston with weight exerts a pressure, p
Water bath maintains a temperature, T

## Slide 6
6
Boyle
Chart: Fix the Temperature and Amount of Gas within a given experiment
| 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60
Expt.1 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5
Expt.2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Expt.3 | 5 | 6.5 | 8 | 9.5 | 11 | 12.5 | 14 | 15.5 | 17
For different temperatures or amounts of gas one gets different slopes. So the slope for Boyle is a function of n and T, SB(n, T).
For all choices of n and T there is the same intercept on the pressure axis. The value is -1.01·105N/m2. Define the absolute pressure;
pabsolute ≡ (Force applied to piston/piston area) - (this value).
pabsolute = pgauge + patmospheric
From now on use pabsolute

## Slide 7
7
Charles
Chart: Fix pressure and amount of gas
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
Expt.1 | 2.73 | 2.83 | 2.93 | 3.03 | 3.13 | 3.23 | 3.33 | 3.43 | 3.53
Expt.2 | 5.46 | 5.66 | 5.86 | 6.06 | 6.26 | 6.46 | 6.66 | 6.86 | 7.06
Expt.3 | 10.92 | 11.32 | 11.72 | 12.12 | 12.52 | 12.92 | 13.32 | 13.72 | 14.12
For different pressures or amounts of gas one gets different slopes. So the slope for Charles is a function of n and p, SC(n, p).
For all choices of n and p there is the same intercept on the temperature axis. The value is -273°C. Define the absolute temperature;
Tabsolute ≡ ( TCelsius ) - (this value).
TKelvin = TCelsius + 273°K
From now on use TKelvin

## Slide 8
8
Gay-Lussac and Avogadro turn out the same way
Gather all four results.
Combine pairs of results to see functional form of slopes.
Combine Boyle and Charles ( or Avogadro and Gay-Lussac ).
Solve each for T and equate.
This can only be true if
Give the constant of proportionality a symbol ( R ), a name ( ideal gas constant ), and find its value using any data set. R = 8.314 J/mol·K

## Slide 9
9
Clicker Question (L23Q2): 3.3 mols of an ideal gas at 0°C and 3.0 atm absolute pressure occupy a volume of V0. If the temperature is raised to 273°C and the volume is decreased to V0/2, what is the new pressure?
A) 9.9 atm B) 6.0 atm
C) 12.0 atm D) 3.0 atm
Clicker Question (L23Q3): Given the same information as above, could you find the volume V0?
A) Yes B) No