## Slide 1: Physics 101 - Lecture 15
Today’s lecture will get us to section 8.6.

## Slide 2: Statics Examples: The Spool, The Ladder, and The Weighted Beam.
Summing forces will be easy but what should I pick for the axis of rotation?
The Spool - Depending upon the angle of the rope, the spool moves to the right or to the left. Find the angle the marks the transition.
θ
P
Ff
mg
N
x
y
+
We will need P in component form.
P
P∙sin(θ)
θ
P∙cos(θ)
Choice A
Choice B
Spool
Notes: Critical angle is about 60 degrees for our spool. Line of action of P passes through point B.

## Slide 3: Try Choice A
Let r be the small radius and R be the large radius.
θ
P
Ff
mg
N
x
y
+
Choice A
Solve the torque equation for Ff and substitute into the ∑Fx equation.
The sign of a could end up as positive or negative depending upon θ.
I want the angle for which the sign of the acceleration is changing. That implies that a = 0.

## Slide 4: Try Choice B
θ
P
θ
Pcos(θ)
axis of rotation
The only solution possible is when the second term is zero.

## Slide 5: Clicker Question: Suppose that you and the ladder have the same mass and the coefficient of friction between floor and ladder is 0.3. Is there a limit to how far up the ladder you may climb? A) Yes B) No C) It depends upon the angle between the wall and the ladder.
Ladder
Notes: Chain gives ability to see size of what would have been the friction force.

## Slide 6: Work out the Ladder Problem
+
x
y
L
L/2
mg
Nw
θ
Ff
Ng
Mg
l
Axis of rotation
Sum the forces and torques.
Add in force models and geometry.
Solve the 1st three for Ff, Ng, and Nw.
Notes: Chain force is represented as friction, Ff.

## Slide 7
Substitute from these three into the Friction Force model.
Solve for l/L.
In our problem we were given M = m and μs = 0.3.
If tan(θ) ≥ 1.2 then we cannot stand on the ladder at all! tan-1(1.2) = 50.2°.
Our ladder is slanted at about 30° with respect to the wall. I also weigh more like 4 times what the ladder does. How should the chain force behave as I stand on the ladder?
If I climb about 70% of the length of the ladder, it should read half of my weight.

## Slide 8: Clicker Question: Test your physical intuition. Don’t compute - just take 30s to try to see the answer. Then we will work it out carefully.
The Weighted Beam Problem
FR
FL
The uniform beam weighs 120N and is 6m long. The uniform block weighs 60N and is 2m from the right end. What is the size of FR?
A) 90N B) 100N
C) 120N D) 180N

## Slide 9: I wonder what I should do first?
FR
FL
+
x
y
60N
120N
Axis of rotation - WHY HERE?
Sum of forces
Sum of torques
Look at that happy result! With a careful choice of the axis of rotation we immediately produce a single equation to solve.