## Slide 1: Lecture 15 Available Work and Free Energy
U
F
-TS
F
U
Notes: 1
http://galileoandeinstein.physics.virginia.edu/more_stuff/flashlets/carnot.htm

## Slide 2: Helpful Hints in Dealing with Engines and Fridges
Sketch the process (see figures below). [Carnot is reversible, St’ling is not!] Define Qh and Qc and Wby (or Won) as positive and show directions of flow.
Determine which Q is given.
Write the First Law of Thermodynamics (FLT), Heat and Work.
We considered three configurations of Carnot cycles:
Qh
Wby
Th
Tc
Qc
Engine: We pay for Qh, we want Wby.
Wby = Qh - Qc = Qh
Carnot:  = 1 - Tc/Th
Qleak= QC
Qh
Won
Th
Tc
Qc
Refrigerator: We pay for Won, we want Qc.
Qc = Qh - Won = Won
Carnot:  = Tc/(Th - Tc)
Qleak= Qh
Qh
Won
Th
Tc
Qc
Heat pump: We pay for Won, we want Qh.
Qh = Qc + Won = Won
Carnot:  = Th/(Th - Tc)
You want big 
These both have large  when Th - Tc is small.
This has large  when Th - Tc is large.
Notes: Based on Entropy and Temperature definition, we know that dQh/dQl>dTh/dTl. Therefore, Efficiency = 1-Ql/Qh < 1-Tc/Th.

## Slide 3: ACT 1: Entropy Change in Heat Pump
Consider a Carnot heat pump. (S of universe is unchanged.)
1) What is the sign of the entropy change of the hot reservoir during one cycle?
a) Sh < 0 b) Sh = 0 c) Sh > 0
2) What is the sign of the entropy change of the cold reservoir?
a) Sc < 0 b) Sc = 0 c) Sc > 0
3) Compare the magnitudes of the two changes.
a) |Sc| < |Sh| b) |Sc| = |Sh| c) |Sc| > |Sh|
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Engine

## Slide 4: Solution
Consider a Carnot heat pump.
1) What is the sign of the entropy change of the hot reservoir during one cycle?
a) Sh < 0 b) Sh = 0 c) Sh > 0
2) What is the sign of the entropy change of the cold reservoir?
a) Sc < 0 b) Sc = 0 c) Sc > 0
3) Compare the magnitudes of the two changes.
a) |Sc| < |Sh| b) |Sc| = |Sh| c) |Sc| > |Sh|
Energy (heat) is entering the hot reservoir, so the
number of available microstates is increasing.
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Engine
Notes: Note: There’s actually also a heat flow OUT of the “hot reservoir” – that’s the leak we are trying to fight.
So, if you take that into account, then in fact there’s NO entropy change of the hot reservoir. But if we include the
environment into which that heat Q_leak is going, then IT’S entropy does increase. Now, maybe that heat leak
goes directly into the cold reservoir (e.g., through the window of the house). Then again, we get a net entropy change, since
the entropy increase of the cold reservoir is more than the entropy decrease of the house. But if we are including this heat
leak channel, then this CANNOT be a Carnot heat pump, since the heat flow from hot to cold is irreversible.

## Slide 5: Solution
Consider a Carnot heat pump.
1) What is the sign of the entropy change of the hot reservoir during one cycle?
a) Sh < 0 b) Sh = 0 c) Sh > 0
2) What is the sign of the entropy change of the cold reservoir?
a) Sc < 0 b) Sc = 0 c) Sc > 0
3) Compare the magnitudes of the two changes.
a) |Sc| < |Sh| b) |Sc| = |Sh| c) |Sc| > |Sh|
Energy (heat) is entering the hot reservoir, so the
number of available microstates is increasing.
Energy (heat) is leaving the cold reservoir.
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Engine
Notes: Note: There’s actually also a heat flow OUT of the “hot reservoir” – that’s the leak we are trying to fight.
So, if you take that into account, then in fact there’s NO entropy change of the hot reservoir. But if we include the
environment into which that heat Q_leak is going, then IT’S entropy does increase. Now, maybe that heat leak
goes directly into the cold reservoir (e.g., through the window of the house). Then again, we get a net entropy change, since
the entropy increase of the cold reservoir is more than the entropy decrease of the house. But if we are including this heat
leak channel, then this CANNOT be a Carnot heat pump, since the heat flow from hot to cold is irreversible.

## Slide 6: Solution
Consider a Carnot heat pump.
1) What is the sign of the entropy change of the hot reservoir during one cycle?
a) Sh < 0 b) Sh = 0 c) Sh > 0
2) What is the sign of the entropy change of the cold reservoir?
a) Sc < 0 b) Sc = 0 c) Sc > 0
3) Compare the magnitudes of the two changes.
a) |Sc| < |Sh| b) |Sc| = |Sh| c) |Sc| > |Sh|
Energy (heat) is entering the hot reservoir, so the
number of available microstates is increasing.
Energy (heat) is leaving the cold reservoir.
It’s a reversible cycle, so Stot = 0. Therefore, the two entropy changes must cancel. Remember that the entropy of the “engine” itself does not change.
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Engine
Note: We’ve neglected the heat leak OUT of the hot reservoir. In fact, this must equal
Qh (why?). If that heat leaks directly into the cold reservior, this will be irreversible…
Notes: Note: There’s actually also a heat flow OUT of the “hot reservoir” – that’s the leak we are trying to fight.
So, if you take that into account, then in fact there’s NO entropy change of the hot reservoir. But if we include the
environment into which that heat Q_leak is going, then IT’S entropy does increase. Now, maybe that heat leak
goes directly into the cold reservoir (e.g., through the window of the house). Then again, we get a net entropy change, since
the entropy increase of the cold reservoir is more than the entropy decrease of the house. But if we are including this heat
leak channel, then this CANNOT be a Carnot heat pump, since the heat flow from hot to cold is irreversible.

## Slide 7: The 2nd Law Sets the Maximum Efficiency (1)
How to calculate Stot?
Over one cycle:
Stot = Sengine + Shot +Scold
Remember: Qh is the heat taken from the hot reservoir, so Shot = -Qh/Th.
Qc is the heat added to the cold reservoir, so Scold = +Qc/Tc.
= 0
From the definition of T
2nd Law
Qc cannot be zero. Some energy is always lost.

## Slide 8: Heat Engine Summary
For all cycles:
For the Carnot cycle:
Carnot (best) efficiency:
Carnot engines are an idealization - impossible to realize. They require very slow processes, and perfect insulation.
When there’s a net entropy increase, the efficiency is reduced:
Some energy is dumped into the cold reservoir.
Qc cannot be reduced to zero.
Only for reversible cycles otherwise = replaced by <.

## Slide 9: ACT 2: Work from a hot brick
We saw that the efficiency of any heat engine is given by  = 1 - Qc/Qh.
Heat a brick to 400 K. Connect it to a Carnot Engine. What is the average efficiency if the cold reservoir is 300 K? The brick has a constant heat capacity of C = 1 J/K.
a)  < 25% b)  = 25% c)  > 25%
Wby
QC
Qh
Brick, 400K
300 K

## Slide 10: Solution
Wby
QC
Qh
Brick, 400 K
300 K
Did you use:  = 1 - Tc/Th ?
If so, you forgot that the brick is cooling (it’s not a constant T reservoir). Therefore, the efficiency (which begins at 25%) drops as the brick cools. We must integrate: (dQh = -CdT) times the efficiency factor…
This is an interesting result. Let’s discuss it.
We saw that the efficiency of any heat engine is given by  = 1 - Qc/Qh.
Heat a brick to 400 K. Connect it to a Carnot Engine. What is the average efficiency if the cold reservoir is 300 K? The brick has a constant heat capacity of C = 1 J/K.
a)  < 25% b)  = 25% c)  > 25%

## Slide 11: Available Work and Free Energy
We just found that the work that the engine can do as the brick cools from its initial temperature to Tc is:
The form of this result is useful enough that we
define a new quantity, the “free energy” of the brick:
Fbrick  Ubrick - TenvSbrick
With this definition, Wby = -Fbrick. This is the best we can do. In general, Wby will be smaller: Wby  -Fbrick = Fi – Ff
Free energy tells how much work can be extracted. It is useful, because it is almost entirely a property of the brick.
Only the temperature of the environment is important.
In the ACT, Tenv was Tc.
Notes: We use T_env, because usually one reservoir is just the environment and the other is the heat source that we’re paying for.

## Slide 12: ACT 3: Work from a cold brick?
Wby
QC
Qh
Brick, 400 K
300 K
We obtained work from a hot brick, initially at 400K. If instead the brick were initially at 200K, could we still do work in our 300K environment?
a) Yes.
b) No, you can’t have Th < Tc.
c) No, we would have to put work in.

## Slide 13: Solution
We obtained work from a hot brick, initially at 400K. If instead the brick were initially at 200K, could we still do work in our 300K environment?
a) Yes.
b) No, you can’t have Th < Tc.
c) No, we would have to put work in.
Wby
QC
Qh
Brick, 400 K
300 K
Wby
QC
Qh
300 K
Brick, 200K
Think outside the box. Use the brick as the cold reservoir:
Question:
Can we use free energy to calculate the work?
Environment

## Slide 14
What is the free energy of an object that is hotter or colder than its environment?
The object is in thermal equilibrium when T = Tenv, so we will compare the free energy at other temperatures to its value at that temperature, since that is where the object will end up.
1) Heat the brick to 310 K. T = +10 K.
FB =
2) Cool the brick to 290 K. T = -10 K.
FB =
Plot the results:
Exercise: Free Energy and Equilibrium
Useful info: Heat Capacity of brick: C = 1kJ / K UB = C T = C(TB - 300K) SB = C ln (TB / 300K) FB = UB - (300K) SB

## Slide 15: Solution
What is the free energy of an object that is hotter or colder than its environment?
The object is in thermal equilibrium when T = Tenv, so we will compare the free energy at other temperatures to its value at that temperature, since that is where the object will end up.
1) Heat the brick to 310 K. T = +10 K.
FB = (1 kJ/K)*(10 K) -(300 K)*(1 kJ/K)*ln(310/300) = 10 kJ - 9.84 kJ = 0.16 kJ
2) Cool the brick to 290 K. T = -10 K.
FB = (1 kJ/K)*(-10 K) -(300 K)*(1 kJ/K)*ln(290/300) = -10 kJ + 10.17 kJ = 0.17 kJ
Plot the results:
Useful info: Heat Capacity of brick: C = 1kJ / K UB = C T = C(TB - 300K) SB = C ln (TB / 300K) FB = UB - (300K) SB =C(T-Te) - CTeln(T/Te)
You can plot (x-300)-300*log(x/300) on your calculator. That’s how I got this graph.
Conclusion:
The free energy of the brick is minimum when its temperature is the temperature of the environment.
Notes: It might be worth mentioning geothermal energy (what’s the temperature of the envireonment?)

## Slide 16: Equilibrium is found at Free Energy Minimum
The free energy is minimum when the system has the same temperature as the environment. Why is F minimized in thermal equilibrium?
Equilibrium corresponds to a maximum in total entropy:
Stot = S + Se
If the system draws dU from the environment, dSe =  dU/Te. So: dStot = dS + dSe = dS - dU / Te = 0 in equilibrium.
= - (dU - TedS) / Te = - dF / Te
So, dStot and dF are proportional to each other with a minus sign (for a given Te). Minimizing F is the same as maximizing Stot. This is not a new physical concept, but F is often a more convenient analysis tool.
S
Se
Te
U
F
-TS
F
U
The two terms in F:
thermal bath

## Slide 17: Caution… Maximum Stot Does Not Always Mean Minimum Fsys
When we introduced the Helmholtz free energy, F, (see the “hot brick” discussion), we assumed that the volume of the brick was constant. If the volume weren’t constant, then the brick could gain or lose energy (and entropy) by contracting or expanding. That would change the analysis.
It is very common that the pressure, not the volume, is constant (e.g., if our system is a gas at constant atmospheric pressure). In this situation, we use a different form of free energy, called “Gibbs free energy”: G = U+pV-TS. The pV term takes into account the work that is done during volume changes.
We won’t use Gibbs free energy in this course, but it important to be aware that the calculation of free energy depends on the situation.

## Slide 18
Free Energy Example
Suppose we have a liter of water at T = 100° C. What is its free energy, if the environment is T = 20° C?
Verify the result by calculating the amount of work we could obtain. Remember that cH2O = 4186 J/kg.K.

## Slide 19
F = U - TS, where T is the temperature of the environment.
U = mcT = 1 kg * 4186 J/kg.K * 80 K = 3.349105 J.
S = mc ln(TH2O/Tenv) = 1011 J/K
F = 3.87104 J
Remember to measure temperature in Kelvin. Otherwise, you’ll get the entropy wrong.
Suppose we have a liter of water at T = 100° C. What is its free energy, if the environment is T = 20° C?
Verify the result by calculating the amount of work we could obtain. Remember that cH2O = 4186 J/kg.K.
Solution

## Slide 20
Solution
If we run a Carnot engine, the efficiency at a given water temperature is:
 = 1 – Tcold /Thot. So, for each small decrease in water temperature, we get this much work out of the engine:
dW = Q = -mc dT
Thus, the total work obtained as T drops from 100° C to 20° C is:
Suppose we have a liter of water at T = 100° C. What is its free energy, if the environment is T = 20° C?
Verify the result by calculating the amount of work we could obtain. Remember that cH2O = 4186 J/kg.K.

## Slide 21:  In many situations maximizing total S (sometimes hard to calculate) to reach equilibrium implies minimizing system free energy (sometimes easier to calculate).  When the system is out of equilibrium, its excess free energy gives the amount of work that an ideal engine could extract from it in a given environment.  Free energy can be tabulated for many materials (e.g., chemical fuels). For the rest of the course we will consider important applications of this principle: Paramagnets (revisited) The law of atmospheres (revisited) Solids: defects and impurities Chemical reactions, especially in gases Carrier densities in semiconductors Adsorption of particles on surfaces Liquid-gas and solid-gas phase transitions
Why is Free Energy important?

## Slide 22: Free Energy Summary
For a Carnot engine: Wby = -U + Te S = -F
from a masssive object
where F = U - TS is called the Helmholtz* free energy of the system referenced to the temperature Te of the environment (or ‘reservoir’).
The free energy of an object is always defined with reference to the temperature of a reservoir, often the environment. An object’s free energy is minimized when its temperature is the same as the environment.
F = U - TS = Free energy  Maximum Available Work
* There are actually several versions of free energy, depending on the particular situation. Helmholtz free energy applies when the system has a constant volume (e.g., a brick). When pressure is constant (e.g., a pot of water open to the air), we use Gibbs Free Energy, G = U + pV - TS. We will not study the other versions in this course.

## Slide 23: Supplement: Gibbs Free Energy
Most phase transitions are observed under constant p,T conditions, not constant-V,T. Unless the stuff is in a closed vessel, it’s open to the air (thus, at atmospheric pressure).
In this case, the entropy of the environment changes not only when the system energy changes but also when its volume changes. The reservoir is (by assumption) in equilibrium at fixed T and p. So, as heat flows, the change of the reservoir’s entropy is:
The change in the total entropy is thus:
where:
In these conditions, maximizing Stot means minimizing the system’s G.
Variables U, V, and S are of the system.
Fixed p and T are of the reservoir.
VR = -V and UR = -U because total volume and total energy are constant.

## Slide 24: Next Monday
 Free Energy and Chemical Potential
 Simple defects in solids
 Ideal gases, revisited