## Slide 1
Act 0
The midterm exam was:
a. Just right b. Too easy c. Too hard
d. Too long
e. Too long and too hard
Notes: Demos:
1. Large standing wave demo without strobe
2. Discharge tubes without diffraction grating handouts

## Slide 2: Lecture 14 Carnot engines, Refrigerators and Heat Pumps
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Heat pump
Heat leak
b
a
p
pb
pa
V
V1 V2
c
d
adiabats
Reading for this Lecture:
Elements Ch 4E-F, 10A-B
Notes: DEMOS:
* Stirling engine driven by hot washer and ice.
* Peltier cooler.

## Slide 3: Heat Engine Efficiency
What’s the best we can do?
The Second Law will tell us.
We pay for the heat input, QH, so:
Define the efficiency
Valid for all heat engines. (Conservation of energy)
Cartoon picture of a heat engine:
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
Wby
Remember:
We define Qh and Qc as positive. The arrows define direction of flow.
Engine

## Slide 4: The 2nd Law Sets the Maximum Efficiency (1)
How to calculate Stot?
Over one cycle:
Stot = Sengine + Shot +Scold
Remember: Qh is the heat taken from the hot reservoir, so Shot = -Qh/Th.
Qc is the heat added to the cold reservoir, so Scold = +Qc/Tc.
= 0
From the definition of T
2nd Law
Qc cannot be zero. Some energy is always lost.

## Slide 5: The 2nd Law Sets the Maximum Efficiency (2)
This is a universal law !! (equivalent to the 2nd law)
It is valid for any procedure that converts thermal energy into work.
We did not assume any special properties (e.g., ideal gas) of the material in the derivation.
The maximum possible efficiency, Carnot = 1 - Tc/Th, is called the Carnot efficiency.
The statement that heat engines have a maximum efficiency was the first expression of the 2nd law, by Sadi Carnot in 1824.

## Slide 6: How Efficient Can an Engine be?
Consider an engine that uses steam (Th = 100° C) as the hot reservoir and ice (Tc = 0° C) as the cold reservoir. How efficient can this engine be?
The Carnot efficiency is
Therefore, an engine that operates between these two temperatures can, at best, turn only 27% of the steam’s heat energy into useful work.
Question: How might we design an engine that has higher efficiency?
Answer: By increasing Th. (That’s more practical than lowering Tc.)
Electrical power plants and race cars obtain better
performance by operating at a much higher Th.
Notes: Show Steam engine and thermoelectric fan here ??

## Slide 7: When Is  Less than Carnot?
Lesson: Avoid irreversible processes.
(ones that increase Stot).
 direct heat flow from hot to cold
 free expansion (far from equilibrium)
 sliding friction
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Engine
We can write the efficiency loss in terms of the change of total entropy:
Carnot

## Slide 8: Heat Engine Summary
For all cycles:
For the Carnot cycle:
Carnot (best) efficiency:
Carnot engines are an idealization - impossible to realize. They require very slow processes, and perfect insulation. When there’s a net entropy increase, the efficiency is reduced:
Some energy is dumped into the cold reservoir.
Qc cannot be reduced to zero.
Only for reversible cycles.

## Slide 9: Act 1: Stirling Efficiency
Will our Stirling engine achieve Carnot efficiency?
a) Yes b) No
V
Tc
Th
Va
Vb
p
1
2
3
4

## Slide 10: Solution
Will our Stirling engine achieve Carnot efficiency?
a) Yes b) No
V
Tc
Th
Va
Vb
p
1
2
3
4
Processes 1 and 3 are irreversible. (isochoric heating and cooling)
1: Cold gas touches hot reservoir.
3: Hot gas touches cold reservoir.
We saw last time, that with Vb = 2Va  = 3/2 (monatomic gas) Th = 373K (boiling water) Tc = 273K (ice water)
For comparison: carnot = 1 – 273/373 = 26.8%

## Slide 11: Example: Gasoline Engine
p
pb
pa
V
V1 V2
Combustion
exhaust / intake
adiabats
b
a
c
d
bc and da are nearly adiabatic processes, because the pistons move too quickly for much heat to flow.
It’s not really a heat engine because the input energy is via fuel injected directly into the engine, not via heat flow. There is no obvious hot reservoir. However, one can still calculate work and energy input for particular gas types.
We can treat the gasoline engine as an Otto cycle:

## Slide 12: Solution
b
a
p
pb
pa
V
V1 V2
c
d
adiabats
Calculate the efficiency:

## Slide 13: Solution
Compression ratio  V2/V1  10  = 1.4 (diatomic gas)  = 60%
(in reality about 30%, due to friction etc.)
b
a
p
pb
pa
V
V1 V2
c
d
adiabats
Write it in terms of volume instead of temperature. We know the volume of the cylinders.
Notes: Why not simply use a higher compression ratio?
  V2 big  huge, heavy engine
  V1 small  temp. gets too high  premature ignition  need to use octane in gas to raise combustion temperature
  In a diesel engine, the combustion is intented to be *caused* by the compression.

## Slide 14: Solution
Why not simply use a higher compression ratio?
 If V2 big, we need a huge, heavy engine (OK for fixed installations).
 If V1 small, the temperature gets too high, causing premature ignition. High compression engines need high octane gas, which has a higher combustion temperature.

## Slide 15: How to Achieve Carnot Efficiency
V
Tc
Th
Vb Va Vc Vd
p
1
2
3
4
To achieve Carnot efficiency, we must replace the isochors (irreversible) with reversible processes. Let’s use adiabatic processes, as shown:
Processes 1 and 3 are now adiabatic.
Processes 2 and 4 are still isothermal.
This cycle is reversible, which means: Stot remains constant:   = Carnot.
This thermal cycle is called the Carnot cycle,
and an engine that implements it is called a
Carnot heat engine.
Notes: http://galileoandeinstein.physics.virginia.edu/more_stuff/flashlets/carnot.htm

## Slide 16: Run the Engine in Reverse
The Carnot cycle is reversible (each step is reversible):
When the engine runs in reverse:
Heat is transferred from cold to hot by action of work on the engine. Note that heat never flows spontaneously from cold to hot; the cold gas is being heated by adiabatic compression (process 3).
Qc / Qh = Tc / Th is still true. (Note: Qh, Qc, and W are still positive!)
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Engine
V
Tc
Th
Vb Va Vc Vd
p
1
2
3
4
Reverse all the arrows
Qh
Qc

## Slide 17: Refrigerators and Heat Pumps
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Engine
Refrigerators and heat pumps are heat engines running in reverse.
How do we measure their performance? It depends on what you want to accomplish.
Refrigerator: We want to keep the food cold (Qc). We pay for W (the electric motor in the fridge).
So, the coefficient of performance, K is:
Heat pump: We want to keep the house warm (Qh). We pay for W (the electric motor in the garden).
The coefficient of performance, K is:
It’s not called “efficiency”.

## Slide 18: Helpful Hints in Dealing with Engines and Fridges
Sketch the process (see figures below). Define Qh and Qc and Wby (or Won) as positive and show directions of flow.
Determine which Q is given.
Write the First Law of Thermodynamics (FLT).
We considered three configurations of Carnot cycles:
Qh
Wby
Th
Tc
Qc
Engine: We pay for Qh, we want Wby.
Wby = Qh - Qc = Qh
Carnot:  = 1 - Tc/Th
Qleak= QC
Qh
Won
Th
Tc
Qc
Refrigerator: We pay for Won, we want Qc.
Qc = Qh - Won = Won
Carnot:  = Tc/(Th - Tc)
Qleak= Qh
Qh
Won
Th
Tc
Qc
Heat pump: We pay for Won, we want Qh.
Qh = Qc + Won = Won
Carnot:  = Th/(Th - Tc)
These both have large  when Th - Tc is small.
This has large  when Th - Tc is large.

## Slide 19
There is a 70 W heat leak (the insulation is not perfect) from a room at temperature 22°C into an ideal refrigerator. How much electrical power is needed to keep the refrigerator at -10° C? Assume Carnot performance.
Act 2: Refrigerator
a) < 70 W
b) = 70 W
c) > 70 W

## Slide 20
Act 2: Refrigerator
There is a 70 W heat leak (the insulation is not perfect) from a room at temperature 22° C into an ideal refrigerator. How much electrical power is needed to keep the refrigerator at -10° C? Assume Carnot performance.
Hint: Qc must exactly compensate for the heat leak.
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Fridge
Heat leak
a) < 70 W
b) = 70 W
c) > 70 W

## Slide 21
We need Qc = 70 J each second.
Therefore we need
The motor power is 8.5 Watts. Watt = Joule/second.
Solution
There is a 70 W heat leak (the insulation is not perfect) from a room at temperature 22° C into an ideal refrigerator. How much electrical power is needed to keep the refrigerator at -10° C? Assume Carnot performance.
Hint: Qc must exactly compensate for the heat leak.
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Fridge
Heat leak
This result illustrates an unintuitive property of refrigerators and heat pumps: When Th - Tc is small, they pump more heat than the work you pay for.
Notes: Comment on the fact that large W is good for an engine, but bad for a refrigerator.

## Slide 22
Supplement: Peltier cooler
Driving a current (~amps) through generates a temperature difference. 20-50˚C typical
Not so common – they’re more costly, take a lot of power, and you still have to get rid of the heat! But....no moving parts to break.
How’s it work…
Electrons pushed from electron-deficit material (p-type) to electron-rich material (n-type); they slow down, cooling the top connector. Similarly, they heat up in going from n to p-type (bottom connector).
Despite the radically different construction, this heat pump must obey exactly the same limits on efficiency as the gas-based pumps, because these limits are based on the 1st and 2nd laws, not any details.

## Slide 23
Refrigerators work less well as Th - Tc becomes large.
The colder you try to go, the less efficient the refrigerator gets. The limit as TC goes to zero is zero efficiency !
Since heat leaks will not disappear as the object is cooled, you need to supply more work the colder it gets. The integral of the power required diverges as Tc  0.
Therefore you cannot cool a system to absolute zero.
The Limits of Cooling
The maximum coefficient of performance is
Notes: Show Peltier cooler: a non-mechanical refrigerator.

## Slide 24
Suppose that the heat flow out of your 20° C home in the winter is 7 kW. If the temperature outside is -15° C, how much power would an ideal heat pump require to maintain a constant inside temperature?
Act 3: Heat Pump
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Heat pump
Heat leak
a) W < 7 kW
b) W = 7 kW
c) W > 7 kW

## Slide 25
We need Qh = 7000 J each second.
Therefore we need
The electric company must supply 836 Watts, much less than the 7 kW that a furnace would require!
Suppose that the heat flow out of your 20° C home in the winter is 7 kW. If the temperature outside is -15° C, how much power would an ideal heat pump require to maintain a constant inside temperature?
Solution
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Heat pump
Heat leak
Beware:
Real heat pumps are not nearly ideal, so the advantage is smaller.
a) W < 7 kW
b) W = 7 kW
c) W > 7 kW
This is what you’d need with an electric blanket or furnace.

## Slide 26: Next Time
Available Work and Free Energy