## Slide 1
Act 0
The midterm exam was:
a. Just right b. Too easy c. Too hard
d. Too long
e. Too long and too hard
Notes: Demos:
1. Large standing wave demo without strobe
2. Discharge tubes without diffraction grating handouts

## Slide 2: Lecture 14 Heat Pumps, Refrigerators, and Bricks!
 Pumping Heat: Heat pumps and Refrigerators
 Available Work and Free Energy
 Work from Hot and Cold Bricks
Reading for this Lecture:
Elements Ch 10
Reading for Lecture 16:
Elements Ch 11
Notes: DEMOS:
* Stirling engine driven by hot washer and ice.
* Peltier cooler.

## Slide 3: Run the Engine in Reverse
The Carnot cycle is reversible (each step is reversible):
When the engine runs in reverse:
Heat is transferred from cold to hot by action of work on the engine. Note that heat never flows spontaneously from cold to hot; the cold gas is being heated by adiabatic compression (process 3).
Qc / Qh = Tc / Th is still true. (Note: Qh, Qc, and W are still positive!)
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Engine
V
Tc
Th
Vb Va Vc Vd
p
1
2
3
4
Reverse all the arrows
Qh
Qc

## Slide 4: Refrigerators and Heat Pumps
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Engine
Refrigerators and heat pumps are heat engines running in reverse.
How do we measure their performance? It depends on what you want to accomplish.
Refrigerator: We want to keep the food cold (Qc). We pay for W (the electric motor in the fridge).
So, the coefficient of performance, K is:
Heat pump: We want to keep the house warm (Qh). We pay for W (the electric motor in the garden).
The coefficient of performance, K is:
It’s not called “efficiency”.

## Slide 5: Helpful Hints in Dealing with Engines and Fridges
Sketch the process (see figures below). Define Qh and Qc and Wby (or Won) as positive and show directions of flow.
Determine which Q is given.
Write the First Law of Thermodynamics (FLT).
We considered three configurations of Carnot cycles:
Qh
Wby
Th
Tc
Qc
Engine: We pay for Qh, we want Wby.
Wby = Qh - Qc = Qh
Carnot:  = 1 - Tc/Th
Qleak= QC
Qh
Won
Th
Tc
Qc
Refrigerator: We pay for Won, we want Qc.
Qc = Qh - Won = Won
Carnot:  = Tc/(Th - Tc)
Qleak= Qh
Qh
Won
Th
Tc
Qc
Heat pump: We pay for Won, we want Qh.
Qh = Qc + Won = Won
Carnot:  = Th/(Th - Tc)
These both have large  when Th - Tc is small.
This has large  when Th - Tc is large.

## Slide 6
There is a 70 W heat leak (the insulation is not perfect) from a room at temperature 22°C into an ideal refrigerator. How much electrical power is needed to keep the refrigerator at -10° C? Assume Carnot performance.
Act 1: Refrigerator
a) < 70 W
b) = 70 W
c) > 70 W

## Slide 7
Act 1: Refrigerator
There is a 70 W heat leak (the insulation is not perfect) from a room at temperature 22° C into an ideal refrigerator. How much electrical power is needed to keep the refrigerator at -10° C? Assume Carnot performance.
Hint: Qc must exactly compensate for the heat leak.
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Fridge
Heat leak
a) < 70 W
b) = 70 W
c) > 70 W

## Slide 8
The coefficient of performance is:
We need Qc = 70 J each second.
Therefore we need
The motor power is 8.5 Watts. Watt = Joule/second.
Solution
There is a 70 W heat leak (the insulation is not perfect) from a room at temperature 22° C into an ideal refrigerator. How much electrical power is needed to keep the refrigerator at -10° C? Assume Carnot performance.
Hint: Qc must exactly compensate for the heat leak.
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Fridge
Heat leak
This result illustrates an unintuitive property of refrigerators and heat pumps: When Th - Tc is small, they pump more heat than the work you pay for.
Notes: Comment on the fact that large W is good for an engine, but bad for a refrigerator.

## Slide 9
Supplement: Peltier cooler
Driving a current (~amps) through generates a temperature difference. 20-50˚C typical
Not so common – they’re more costly, take a lot of power, and you still have to get rid of the heat! But....no moving parts to break.
How’s it work…
Electrons pushed from electron-deficit material (p-type) to electron-rich material (n-type); they slow down, cooling the top connector. Similarly, they heat up in going from n to p-type (bottom connector).
Despite the radically different construction, this heat pump must obey exactly the same limits on efficiency as the gas-based pumps, because these limits are based on the 1st and 2nd laws, not any details.

## Slide 10
Refrigerators work less well as Th - Tc becomes large.
The colder you try to go, the less efficient the refrigerator gets. The limit as TC goes to zero is zero efficiency !
Since heat leaks will not disappear as the object is cooled, you need to supply more work the colder it gets. The integral of the power required diverges as Tc  0.
Therefore you cannot cool a system to absolute zero.
The Limits of Cooling
The maximum efficiency is
Notes: Show Peltier cooler: a non-mechanical refrigerator.

## Slide 11
Suppose that the heat flow out of your 20° C home in the winter is 7 kW. If the temperature outside is -15° C, how much power would an ideal heat pump require to maintain a constant inside temperature?
Exercise: Heat Pump
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Heat pump
Heat leak
a) W < 7 kW
b) W = 7 kW
c) W > 7 kW

## Slide 12
The coefficient of performance is:
We need Qh = 7000 J each second.
Therefore we need
The electric company must supply 836 Watts, much less than the 7 kW that a furnace would require!
Suppose that the heat flow out of your 20° C home in the winter is 7 kW. If the temperature outside is -15° C, how much power would an ideal heat pump require to maintain a constant inside temperature?
Solution
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Heat pump
Heat leak
Beware:
Real heat pumps are not nearly ideal, so the advantage is smaller.
a) W < 7 kW
b) W = 7 kW
c) W > 7 kW
This is what you’d need with an electric blanket or furnace.

## Slide 13: ACT 2: Work from a hot brick
We saw that the efficiency of any heat engine is given by  = 1 - Qc/Qh.
Heat a brick to 400 K. Connect it to a Carnot Engine. What is the average efficiency if the cold reservoir is 300 K? The brick has a constant heat capacity of C = 1 J/K.
a)  < 25% b)  = 25% c)  > 25%
Wby
QC
Qh
Brick, 400K
300 K

## Slide 14: Solution
Wby
QC
Qh
Brick, 400 K
300 K
Did you use:  = 1 - Tc/Th ?
If so, you missed that the brick is cooling (it’s not a constant T reservoir). Therefore, the efficiency (which begins at 25%) drops as the brick cools. We must integrate: (dQh = -CdT)
This is an interesting result. Let’s discuss it.
We saw that the efficiency of any heat engine is given by  = 1 - Qc/Qh.
Heat a brick to 400 K. Connect it to a Carnot Engine. What is the average efficiency if the cold reservoir is 300 K? The brick has a constant heat capacity of C = 1 J/K.
a)  < 25% b)  = 25% c)  > 25%

## Slide 15: Available Work and Free Energy
We just found that the work that the engine can do as the brick cools from its initial temperature to Tc is:
The form of this result is useful enough that we
define a new quantity, the “free energy” of the brick:
Fbrick  Ubrick - TenvSbrick
With this definition, Wby = -Fbrick. This is the best we can do. In general, Wby will be smaller: Wby  -Fbrick = Fi – Ff
Free energy tells how much work can be extracted. It is useful, because it is almost entirely a property of the brick.
Only the temperature of the environment is important.
In the ACT, Tenv was Tc.
Notes: We use T_env, because usually one reservoir is just the environment and the other is the heat source that we’re paying for.

## Slide 16: ACT 3: Work from a cold brick?
Wby
QC
Qh
Brick, 400 K
300 K
We obtained work from a hot brick, initially at 400K. If instead the brick were initially at 200K, could we still do work in our 300K environment?
a) Yes.
b) No, you can’t have Th < Tc.
c) No, we would have to put work in.
Hint: Fill in the diagram:

## Slide 17: Solution
We obtained work from a hot brick, initially at 400K. If instead the brick were initially at 200K, could we still do work in our 300K environment?
a) Yes.
b) No, you can’t have Th < Tc.
c) No, we would have to put work in.
Wby
QC
Qh
Brick, 400 K
300 K
Wby
QC
Qh
300 K
Brick, 200K
Think outside the box. Use the brick as the cold reservoir:
Question:
Can we use free energy to calculate the work?
Environment

## Slide 18
What is the free energy of an object that is hotter or colder than its environment?
The object is in thermal equilibrium when T = Tenv, so we will compare the free energy at other temperatures to its value at that temperature, since that is where the object will end up.
1) Heat the brick to 310 K. T = +10 K.
FB =
2) Cool the brick to 290 K. T = -10 K.
FB =
Plot the results:
Exercise: Free Energy and Equilibrium
Useful info: Heat Capacity of brick: C = 1kJ / K UB = C T = C(TB - 300K) SB = C ln (TB / 300K) FB = UB - (300K) SB

## Slide 19: Solution
What is the free energy of an object that is hotter or colder than its environment?
The object is in thermal equilibrium when T = Tenv, so we will compare the free energy at other temperatures to its value at that temperature, since that is where the object will end up.
1) Heat the brick to 310 K. T = +10 K.
FB = (1 kJ/K)*(10 K) -(300 K)*(1 kJ/K)*ln(310/300) = 10 kJ - 9.84 kJ = 0.16 kJ
2) Cool the brick to 290 K. T = -10 K.
FB = (1 kJ/K)*(-10 K) -(300 K)*(1 kJ/K)*ln(290/300) = -10 kJ + 10.17 kJ = 0.17 kJ
Plot the results:
Useful info: Heat Capacity of brick: C = 1kJ / K UB = C T = C(TB - 300K) SB = C ln (TB / 300K) FB = UB - (300K) SB =C(T-Te) - CTeln(T/Te)
You can plot (x-300)-300*log(x/300) on your calculator. That’s how I got this graph.
Conclusion:
The free energy of the brick is minimum when its temperature is the temperature of the environment.
Notes: It might be worth mentioning geothermal energy (what’s the temperature of the envireonment?)

## Slide 20: Equilibrium is found at Free Energy Minimum
The free energy is minimum when the system has the same temperature as the environment. Why is F minimized in thermal equilibrium?
Equilibrium corresponds to a maximum in total entropy:
Stot = S + Se
If the system draws dU from the environment, dSe =  dU/Te. So:
dStot = dS + dSe = dS - dU / Te = 0 in equilibrium.
= - (dU - TedS) / Te = - dF / Te
So, dStot and dF are proportional to each other with a minus sign (for a given Te). Minimizing F is the same as maximizing Stot. This is not a new physical concept, but F is often a more convenient analysis tool.
S
Se
Te
U
F
-TS
F
U
The two terms in F:

## Slide 21:  In many situations maximizing total S (sometimes hard to calculate) to reach equilibrium implies minimizing system free energy (sometimes easier to calculate).  When the system is out of equilibrium, its excess free energy gives the amount of work that an ideal engine could extract from it in a given environment.  Free energy can be tabulated for many materials (e.g., chemical fuels). For the rest of the course we will consider important applications of this principle: Paramagnets (revisited) The law of atmospheres (revisited) Solids: defects and impurities Chemical reactions, especially in gases Carrier densities in semiconductors Adsorption of particles on surfaces Liquid-gas and solid-gas phase transitions
Why is Free Energy important?

## Slide 22: Free Energy Summary
For a Carnot engine: Wby = -U + Te S = -F
where F = U - TS is called the Helmholtz* free energy of the system referenced to the temperature Te of the environment (or ‘reservoir’).
The free energy of an object is always defined with reference to the temperature of a reservoir, often the environment. An object’s free energy is minimized when its temperature is the same as the environment.
F = U - TS = Free energy  Maximum Available Work
* There are actually several versions of free energy, depending on the particular situation. Helmholtz free energy applies when the system has a constant volume (e.g., a brick). When pressure is constant (e.g., a pot of water open to the air), we use Gibbs Free Energy, G = U + pV - TS. We will not study the other versions in this course.

## Slide 23: Caution… Maximum Stot Does Not Always Mean Minimum Fsys
When we introduced the Helmholtz free energy, F, (see the “hot brick” discussion), we assumed that the volume of the brick was constant. If the volume weren’t constant, then the brick could gain or lose energy (and entropy) by contracting or expanding. That would change the analysis.
It is very common that the pressure, not the volume, is constant (e.g., if our system is a gas at constant atmospheric pressure). In this situation, we use a different form of free energy, called “Gibbs free energy”: G = U+pV-TS. The pV term takes into account the work that is done during volume changes.
We won’t use Gibbs free energy in this course, but it important to be aware that the calculation of free energy depends on the situation.

## Slide 24: Supplement: Gibbs Free Energy
Most phase transitions are observed under constant p,T conditions, not constant-V,T. Unless the stuff is in a closed vessel, it’s open to the air (thus, at atmospheric pressure).
In this case, the entropy of the environment changes not only when the system energy changes but also when its volume changes. The reservoir is (by assumption) in equilibrium at fixed T and p. So, as heat flows, the change of the reservoir’s entropy is:
The change in the total entropy is thus:
where:
In these conditions, maximizing Stot means minimizing the system’s G.
Variables U, V, and S are of the system.
Fixed p and T are of the reservoir.
VR = -V and UR = -U because total volume and total energy are constant.

## Slide 25: Next Monday
 Free Energy and Chemical Potential
 Simple defects in solids
 Ideal gases, revisited