## Slide 1
Semiconductors, intrinsic and doped
Reference for this Lecture:
Elements Ch 12
Reference for Lecture 19:
Elements Ch 13
Lecture 17 Applications of Free Energy Minimum

## Slide 2: Last Time
Thumbnail review of free energy: Equilibrium corresponds to maximum Stot = Sreservoir + Ssmall system. When we calculate S, we only need to know the temperature of the reservoir. In minimizing F (equivalent to maximizing Stot) we don’t have to deal explicitly with Sreservoir .
Consider exchange of material (particles) between two containers. These are two small systems in equilibrium with a reservoir (not shown) at temperature T. In equilibrium, dF/dN1 = 0:
The derivative of free energy with respect to particle number is so important that we define a special name and symbol for it:
For two subsystems exchanging particles, the equilibrium condition is:
Maximum Total Entropy Minimum Free Energy Equal chemical potentials
1
N
F = F1+F2
N
1
N
2
The chemical potential of subsystem “i”

## Slide 3: Electrons in Semiconductors
In many materials, electrons cannot have every conceivable energy. There is a low energy range (the “valence band”) and a high energy range (the “conduction band”). A “gap” of disallowed energies separates them. (The reason for the gap is a Physics 214 topic.)
At T = 0, every valence band state is occupied. At T  0, electrons are thermally excited from the valence band to the conduction band. How many determines the electrical conductivity.
The activated free electrons and the “holes” (unfilled states) left behind act as two ideal gases. We can compute the density of thermally excited electrons (and holes) by minimizing Felectron + Fhole .
Here, to simplify the problem we assume that excitation from valence to conduction band always requires the same energy, i.e., every conduction state has energy  more than every valence state. This avoids having to do integrals.
Energy gap, 
At T = 0:
Conduction band has no electrons
Valence band totally filled with electrons
Notes: http://www.ece.utep.edu/courses/ee3329/ee3329/Studyguide/Shockwave/Fundamentals/Demos/Donor.html
http://www.ece.utep.edu/courses/ee3329/ee3329/Studyguide/Shockwave/Fundamentals/Demos/acceptor.html

## Slide 4
Electrons in Semiconductors (2)
This is Shockley’s* cartoon of an intrinsic semiconductor. At T = 0, the cars (electrons) can’t move. If some are raised to the upper level (the conduction band) then motion becomes possible.
The vacant spaces on the lower level are “holes”. Motion of the cars on the lower level is more simply described by pretending that the holes are the objects that move.
*John Bardeen, Walter Brattain, and William Shockley invented the transistor in 1947.
Conduction electron
Hole
An intrinsic semiconductor is one in which the number of electrons equals the number of valence band states, so that at T = 0 every state is filled, and no electrons are left over.
Notes: Redbox  Pauli Exclusion principle states only 1 electron per state (every energy has 2 states, spin up and down)

## Slide 5
We have N electrons N valence states (call their energy zero) N conduction states (energy )
We want to know Ne and Nh, the numbers of conduction electrons and holes at temperature T
Our analysis will be similar to the “Defects in a Lattice” problem.
Conduction electrons and holes are created in pairs, so: Ne = Nh (and dNe = dNh )
Method: Minimize F = Fe + Fh:
Conduction electron

hole
Intrinsic Semiconductors
One big difference: electrons and holes actually behave like ideal gases --they are free to rapidly move around in the crystal, with an “effective mass” me, mh.
So, what are S, F, and  for an Ideal Gas of Particles?

## Slide 6: How Do S, F,  Depend on N/V?
In general, this is a complicated function of particle properties and the environment. To keep things simple, we’ll only work with ideal gases.
For an ideal gas the internal energy per particle, u  U/N, depends on T, but not on N. For many problems we can set this to 0.
How does S depend on N? Let’s count microstates and see.
Thus,
and the chemical potential for an ideal (monatomic) gas is:
n  N/V = particle density, nQ  M/V = number of states per unit volume. nQ can only be calculated using quantum mechanics, so we will treat it as an empirical quantity (i.e., we’ll tell you the numerical value when necessary). nQ is a function of T, but not of the particle density, n.
The number of “bins”, M, is proportional to V. It also depends on T (see next slide).
For ideal gases,  ~ logarithm of particle density.
Notes: density of states == how many states per volume (real space and momentum space)
No limit for classical physics; quantum mechanics does limit this (only certain states allowed). n_T ~ 1/lambda^3
Since we will often only care about difference in mu, we actually won’t usually need to know what n_T is.

## Slide 7: What is nQ?
Considering both position and momentum.
nQ = total no. states (per unit volume) available to a particle at temp. T
QM: particle with momentum p has wavelength = h/p. (h = Plank’s constant)
Taking  as a characteristic length, the effective cell volume is ~V  3 = (h/p)3.
Using p2/2m = (3/2)kT, the quantum-mechanical ‘cell density’ has a T-dependence:
nQ  1/3 = (3mkT/h2)3/2
Examples:
*For a monatomic gas, the nT(T) we had before is nQ; otherwise there are modifications.
If we do the problem more carefully (see Elements for details) we find*

## Slide 8
We just saw that the quantum density for an ideal monatomic gas of particles of mass m, at temperature T, is given by
What is the quantum density nQ,e for a ‘gas’ of electrons at T = 300K, taking into account their spin? (mp = 1837 me)
a) 1.27 x 1025/m3
b) 2.54 x 1025/m3
c) 5.45 x 1026/m3
d) 1.84 x 1033/m3
e) 7.87 x 1034/m3
Act 1

## Slide 9
We just saw that the quantum density for an ideal monatomic gas of particles of mass m, at temperature T, is given by
What is the quantum density nQ,e for a ‘gas’ of electrons, taking into account their spin? (mp = 1837 me)
a) 1.27 x 1025/m3
b) 2.54 x 1025/m3
c) 5.45 x 1026/m3
d) 1.84 x 1033/m3
e) 7.87 x 1034/m3
Solution
If we have more complicated particles (e.g., diatomic molecules that can rotate), this will also increase the quantum density.
See Textbook for more details.
A direct calculation using the above formula would give choice a). But we also need to take into account that every electron spin could be either up or down, i.e., increasing the number of states by a factor of 2.

## Slide 10: Electrons and holes in Semiconductors
We now have the tools to solve for the equilibrium density of e-h pairs:
1. Since they act like ideal gases, the chemical potentials are
2. Electrons and holes are created in pairs total free energy is minimized when
3. For a pure semiconductor, ne = nh = ni (“intrinsic pair density”)
Energy gap, 
At T = 0:
Conduction band has no electrons
Valence band totally filled with electrons
E = 
E = 
nQ = (geometric mean of nQenQh)  (nQenQh)1/2.
Compare to I-V result (p. 11).

## Slide 11
E-h pair density vs. T
In a pure semiconductor, there are equal numbers of conduction-band electrons and valence-band holes:
This “intrinsic density” ni clearly varies strongly with energy gap.
Some numerical values (at T = 300 K):
material (eV) nQ (meter-3) ni (meter-3)
Si 1.14 1.72 x 1025 5.2 x 1015
Ge 0.67 7.21 x 1024 -
GaAs 1.43 2.63 x 1024 -
Question: Why aren’t the nQ all equal? In particular, if you set m = me in the formula, nQ= 1.271025. The answer is that the effective mass of a hole is not equal to the effective mass of an electron (and even me,effective ≠ me 9.11 x 10-31kg!), due to interactions with the lattice. Therefore, we will treat nQ as an empirical quantity.
Notes: Point out for comparison, that ni,Cu ~ 1028/m3. About ten trillion times larger.

## Slide 12: Exercise: Intrinsic Silicon
At 300 K the intrinsic carrier density in Si is ni = 5.2 x 1015/m3, with a bandgap of  = 1.14 eV, and quantum density nQ = 1.72 x 1025/m3.
What is the carrier density at 150 K?
a. 4.3  105/m3 b. 3.4  1010/m3 c. 2.6  1015/m3
Notes: Demo – measure resistance of carbon resistor – dunk in LN  lower T, not many carriers, high R.
Note – this means that some electronics may not work well at cryogenic temps (problem, e.g., for spacecraft design.

## Slide 13: Solution
Exponential sensitivity to temperature!
Change to nQ(T) relatively minor
This is very rapid variation. To get a feeling for it, consider T  301 K (an 0.3% change). Then 5.2  5.6 (a 7.6% change!)
At 300 K the intrinsic carrier density in Si is ni = 5.2 x 1015/m3, with a bandgap of  = 1.14 eV, and quantum density nQ = 1.72 x 1025/m3.
What is the carrier density at 150 K?
a. 4.3105/m3 b. 3.41010/m3 c. 2.61015/m3
For comparison, there are 51028 Si atoms/m3
 even at 300K only 10-13 electrons are excited.
Notes: Demo – measure resistance of carbon resistor – dunk in LN  lower T, not many carriers, high R.
Note – this means that some electronics may not work well at cryogenic temps (problem, e.g., for spacecraft design.

## Slide 14: Digital Thermometers
The rapid (exponential) variation of resistance with temperature is used to measure temperature. Many modern digital thermometers use a “thermistor”, a semiconductor device whose resistance depends on temperature.
Notes: Thermometer demo

## Slide 15
Act 2: Other Semiconductors
Compare the number of intrinsic carriers in the conduction band, ni, for Si, Ge and GaAs at 300 K. Note: kT = 0.026eV at T = 300K.
Some numerical values (at T = 300 K):
material (eV) nQ (meter-3) ni (meter-3)
Si 1.14 1.72 x 1025 5.2 x 1015
Ge 0.67 7.21 x 1024 -
GaAs 1.43 2.63 x 1024 -
a) ni,Si > ni,GaAs > ni,Ge
b) ni,Si > ni,Ge > ni,GaAs
c) ni,Ge > ni,Si > ni,GaAs

## Slide 16
Act 2: Other Semiconductors
Compare the number of intrinsic carriers in the conduction band, ni, for Si, Ge and GaAs at 300 K. Note: kT = 0.026eV at T = 300K.
Some numerical values (at T = 300 K):
material (eV) nQ (meter-3) ni (meter-3)
Si 1.14 1.72 x 1025 5.2 x 1015
Ge 0.67 7.21 x 1024 -
GaAs 1.43 2.63 x 1024 -
a) ni,Si > ni,GaAs > ni,Ge
b) ni,Si > ni,Ge > ni,GaAs
c) ni,Ge > ni,Si > ni,GaAs
The difference is almost entirely due to the band gap.

## Slide 17
At T = 0, in a pure semiconductor the valence band is completely filled with electrons, and there are none in the conduction band. Suppose we replace one Si atom with a P atom. Phosphorous has one more electron, which is very weakly bound (its  is very small), and will almost certainly end up in the conduction band. Think of Shockley’s garage. If we add one car, it will have to go into the upper level, and there are still no vacancies (holes) in the lower level. Phosphorus is called a “donor atom”.
The addition of impurities that have a different number (more or fewer) of valence electrons is called doping. It can have a dramatic effect on the material’s electrical properties.
With doping, we no longer have Ne = Nh. Instead, N’e= N’h + Nd, where Nd is the number of donor atoms.
Silicon (Group IV)
Phosphorous (Group V)
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
P
An extra (free) electron. No extra hole.
Doping of Semiconductors
More of Shockley’s cartoon
Notes: Show applets:
http://www.ece.utep.edu/courses/ee3329/ee3329/Studyguide/Shockwave/Fundamentals/Demos/Donor.html
http://www.ece.utep.edu/courses/ee3329/ee3329/Studyguide/Shockwave/Fundamentals/Demos/acceptor.html
binding energy for phosporous electron is ~0.045eV.
coincidentally, binding energy for boron ‘hole’ is also ~0.045eV.
Note: this corresponds to kT of 532K. If there were only ONE site for the electron to go, then most of the time it *wouldn’t* be excited.
But the conduction band has many empty sites. Therefore, at room temperature,

## Slide 18
2. We can also replace Si atoms with Al. Aluminum has one fewer electron than silicon. What is the relation between Ne and Nh in this case?
a) Ne = Nh - NAl b) Ne = Nh c) Ne = Nh + NAl
Silicon (Group IV)
Aluminum (Group III)
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Al
Act 3
1. There are 51028 Si atoms/m3. At 300 K, ni,Si = 5.2 x 1015/m3. If we replace one out of every million Si atoms with P, how much will the conductivity increase?
a) 104 b) 106 c) 107
Notes: Show applets:
http://www.ece.utep.edu/courses/ee3329/ee3329/Studyguide/Shockwave/Fundamentals/Demos/Donor.html
http://www.ece.utep.edu/courses/ee3329/ee3329/Studyguide/Shockwave/Fundamentals/Demos/acceptor.html

## Slide 19
2. We can also replace Si atoms with Al. Aluminum has one fewer electron than silicon. What is the relation between Ne and Nh in this case?
a) Ne = Nh - NAl b) Ne = Nh c) Ne = Nh + NAl
Silicon (Group IV)
Aluminum (Group III)
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Al
Solution
1. There are 51028 Si atoms/m3. At 300K, ni,Si = 5.2 x 1015/m3. If we replace one out of every million Si atoms with P, how much will the conductivity increase?
a) 104 b) 106 c) 107
ne = ni + nd = ni + 10-6 nSi  10-6 nSi = 5 x 1022/m3, 7 orders of magnitude more than with no doping.
Notes: Show applets:
http://www.ece.utep.edu/courses/ee3329/ee3329/Studyguide/Shockwave/Fundamentals/Demos/Donor.html
http://www.ece.utep.edu/courses/ee3329/ee3329/Studyguide/Shockwave/Fundamentals/Demos/acceptor.html

## Slide 20
2. We can also replace Si atoms with Al. Aluminum has one fewer electron than silicon. What is the relation between Ne and Nh in this case?
a) Ne = Nh - NAl b) Ne = Nh c) Ne = Nh + NAl
Silicon (Group IV)
Aluminum (Group III)
Si
Si
Si
Si
Si
Si
Si
Si
Si
Si
Al
Solution
We are missing some valence electrons, so even when Ne (electrons in the conduction band) is zero, we have one hole per Aluminum atom. Look at the “p-type” part of Shockley’s cartoon.
Aluminum is called an “acceptor atom”. In the equations, acceptors act like negative Nd.
1. There are 51028 Si atoms/m3. At 300K, ni,Si = 5.2 x 1015/m3. If we replace one out of every million Si atoms with P, how much will the conductivity increase?
a) 104 b) 106 c) 107
ne = ni + nd = ni + 10-6 nSi  10-6 nSi = 5 x 1022/m3, 7 orders of magnitude more than with no doping.

## Slide 21
We can follow the same procedure to minimize the free energy.
Assume nd<<nQ. (This is called “light doping”.) F = 0 implies that e + h = 0.
This is again like the vacancy-interstitial problem.
Solution: or nenh = ni2
Typically, nd >> ni. Therefore ne = ni + nd  nd. Almost all of the “free” (conduction) electrons come from the dopant atoms.
For Si at T = 300 K:
If there were no doping, both ne/nQ and nh/nQ would be ~310-9. Even a small amount of doping: nd/nQ = 10-7, increases ne dramatically and suppresses nh. ne/nQ ~ 10-7, nh/nQ ~ 10-12.
In the I-V problem, adding interstitial atoms to a crystal reduces the number of vacancies.
Doping of Semiconductors (2)
ne = nh + nd Assume: ne and nh << nQ.
This is an example of “the law of mass action”.
“intrinsic pair density” ni = ne = nh
nQ= (nQenQh)1/2
Notes: point out that ne ~ ni + n d ~ nd.

## Slide 22
if ne and nh << nQ.
Pure (intrinsic) semiconductor
ne = nh = ni = nQ e-/2kT ni is called the “intrinsic carrier concentration”
= intrinsic e-h pair concentration
Doped semiconductor
ne = nh + nd
nenh = ni2 The law of mass action. This is valid for intrinsic and doped semiconductors.
Summary: Particle equilibrium in Semiconductors

## Slide 23: Example: Law of Mass Action
The addition of impurities increases the crystal’s conductivity. Let’s add nd = 1024/m3 phosphorous atoms to Si. Using the intrinsic carrier density, nI, that we calculated for silicon, compute the density of holes, nh , in this “doped” crystal.
Notes: point out that ne = ni + n d ~ nd.

## Slide 24: Solution
nI = 5.21015 << nd, so ne  nd. This doping overwhelms the intrinsic carrier density.
ne  nh, but nenh = ni2 still holds.
The addition of electrons has depressed the density of holes by over 8 orders of magnitude!
Law of Mass Action 
Question: Is 1024 atoms/m3 a lot or a little? Hint: There are 51028 Si atoms/m3.
The addition of impurities increases the crystal’s conductivity. Let’s add nd = 1024/m3 phosphorous atoms to Si produces. Using the intrinsic carrier density, nI, that we calculated for silicon, compute the density of holes, nh , in this “doped” crystal.

## Slide 25: Act 4
Suppose you have a piece of “dirty” silicon, with lots of unwanted phosphorous impurities (making the conductivity too high because there are too many free electrons). What might you do to fix this?
a) dope with more phosphorous
b) dope with a different type of donor
c) dope with an acceptor atom, like boron

## Slide 26: Solution
Suppose you have a piece of “dirty” silicon, with lots of unwanted phosphorous impurities (making the conductivity too high because there are too many free electrons). What might you do to fix this?
a) dope with more phosphorous
b) dope with a different type of donor
c) dope with an acceptor atom, like boron
Adding more donors will only make the problem worse. Adding more acceptor atoms, we increase the number of holes. Since nenh = constant, increasing the number of holes decreases the number of free electrons.
This technique is called “compensation”.

## Slide 27: Next Monday
 Chemical equilibria - Law of mass action again
 Surface chemistry
 Phase equilibria and chemical potentials