## Slide 1: Lecture 13 Heat Engines
 Thermodynamic processes and entropy
 Thermodynamic cycles
 Extracting work from heat
- How do we define engine efficiency?
- Carnot cycle: the best possible efficiency
Reading for this Lecture:
Elements Ch 4D-E, 10A-B
Notes: 1
DEMOS:
* Stirling (hand held) - no time for the other Stirling engine.
* Thermolectric powered fan
* Steam engine

## Slide 2: Review Entropy in Macroscopic Systems
Traditional thermodynamic entropy: S = k ln = k
We want to calculate S from macrostate information (p, V, T, U, N, etc.) Start with the definition of temperature in terms of entropy:
The entropy changes when T changes: (We’re keeping V and N fixed.)
If CV is constant:

## Slide 3: Entropy in Quasi-static Heat Flow
When V is constant: dS  dU/T = dQ/T  W = 0, so dU = dQ
In fact, dS = dQ/T during any reversible (quasi-static) process, even if V changes.
The reason: In a reversible process, Stot (system plus environment) doesn’t change:
for any reversible process
Stot = 0 if process is reversible.
The reservoir is supplying (or absorbing) heat.
The reservoir’s energy gain is the system’s heat loss. That’s how they interact.

## Slide 4: S in Isothermal Processes
p
V
1
2
T=constant
Suppose V & p change but T doesn’t.
Work is done (dWby = pdV). Heat must enter to keep T constant: dQ = dU+dWby.
So:
Special case, ideal gas:
For an ideal gas, if dT = 0, then dU = 0.
Remember: This holds for quasi-static processes, in which the system remains near thermal equilibrium at all times.
Notes: Why? Because number of states ~V^N

## Slide 5: ACT 1
1) The entropy of a gas increases during a quasi-static isothermal expansion. What happens to the entropy of the environment?
a) Senv < 0 b) Senv = 0 c) Senv > 0
2) Consider instead the ‘free’ expansion (i.e., not quasi-static) of a gas. What happens to the total entropy during this process?
a) Stot < 0 b) Stot = 0 c) Stot > 0
vacuum
Remove the barrier
gas

## Slide 6: Solution
1) The entropy of a gas increases during a quasi-static isothermal expansion. What happens to the entropy of the environment?
a) Senv < 0 b) Senv = 0 c) Senv > 0
2) Consider instead the ‘free’ expansion (i.e., not quasi-static) of a gas. What happens to the total entropy during this process?
a) Stot < 0 b) Stot = 0 c) Stot > 0
vacuum
Remove the barrier
gas
Energy (heat) leaves the environment, so its entropy decreases. In fact, since the environment and gas have the same T, the two entropy changes cancel: Stot = 0. This is a reversible process.

## Slide 7: Solution
1) The entropy of a gas increases during a quasi-static isothermal expansion. What happens to the entropy of the environment?
a) Senv < 0 b) Senv = 0 c) Senv > 0
2) Consider instead the ‘free’ expansion (i.e., not quasi-static) of a gas. What happens to the total entropy during this process?
a) Stot < 0 b) Stot = 0 c) Stot > 0
Energy (heat) leaves the environment, so its entropy decreases. In fact, since the environment and gas have the same T, the two entropy changes cancel: Stot = 0. This is a reversible process.
There is no work or heat flow, so Ugas is constant.  T is constant. However, because the volume increases, so does the number of available states, and therefore Sgas increases. Nothing is happening to the environment. Therefore Stot > 0. This is not a reversible process.

## Slide 8: Quasi-static Adiabatic Processes
Q = 0 (definition of an adiabatic process)
V and T both change as the applied pressure changes.
For example, if p increases (compress the system):
 V decreases, and the associated S also decreases.  T increases, and the associated S also increases.
These two effects must exactly cancel !!
Why? Because:
 This is a reversible process, so Stot = 0.  No other entropy is changing. (Q = 0, and Wby just moves the piston.)
So, in a quasi-static adiabatic process, S = 0.
Note: We did not assume that the system is an ideal gas. This is a general result.
system
Insulated walls
p
V
1
2
TH
TC
Notes: they will show this explicitly in HW for an ideal gas

## Slide 9: Irreversible Processes
Entropy-increasing processes are irreversible,
because the reverse processes would reduce entropy.
Examples:
 Free-expansion (actually, any particle flow between regions of different density)
 Heat flow between two systems with different temperatures.
Consider the four processes of interest here:
Isothermal: Heat flow but no T difference. Reversible
Adiabatic: Q = 0. No heat flow at all. Reversible
Isochoric & Isobaric: Heat flow between different T’s. Irreversible
(Assuming that there are only two reservoirs.)
reversible reversible irreversible irreversible
V
p
isotherm
adiabat
V
p
isochor
V
p
isobar
V
p

## Slide 10: Two blocks, each with heat capacity* C = 1 J/K are initially at different temperatures, T1 = 250 K, T2 = 350 K. They are then placed into contact, and eventually reach a final temperature of 300 K. (Why?) What can you say about the total change in entropy Stot? a) Stot < 0 b) Stot = 0 c) Stot > 0
ACT 2
T1
T2
Tf
Tf
T1 = 250K
T2 = 350K
Tf = 300 K
Two masses each with heat capacity C = 1J/K*
*For a solid, C = CV = Cp, to good approximation, since V  0.

## Slide 11: Two blocks, each with heat capacity* C = 1 J/K are initially at different temperatures, T1 = 250 K, T2 = 350 K. They are then placed into contact, and eventually reach a final temperature of 300 K. (Why?) What can you say about the total change in entropy Stot? a) Stot < 0 b) Stot = 0 c) Stot > 0
Solution
T1
T2
Tf
Tf
T1 = 250K
T2 = 350K
Tf = 300 K
Two masses each with heat capacity C = 1J/K*
*For a solid, C = CV = Cp, to good approximation, because V  0.
This is an irreversible process, so there must be a net increase in entropy. Let’s calculate S:
The positive term is slightly bigger than the negative term.

## Slide 12: A Review of Some Thermodynamic Processes of an Ideal Gas
Isochoric (constant volume)
V
p
1
2
Q
Temperature changes
V
p
1
2
Q
p
Temperature and volume change
Isobaric (constant pressure)
We will assume ideal gases in our treatment of heat engines, because that simplifies the calculations.

## Slide 13
p
V
1
2
Q
Thermal Reservoir
T
Volume and pressure change
p
V
1
2
Volume, pressure and temperature change
Isothermal (constant temperature)
Review (2)
Adiabatic (no heat flow)

## Slide 14: Closed Thermodynamic Cycles
V
p
1
2
3
A closed cycle is one in which the system returns to the initial state. (same p, V, and T) For example:
 U is a state function. Therefore:
 The net work is the enclosed area.
 Energy is conserved (1st Law):
Closed cycles will form the basis of our heat engine discussion.
This is the reason that neither W nor Q is a state function. It makes no sense to talk about a state having a certain amount of W.
Though of course we could use any curves to make a closed cycle, here we will consider
isochoric, isobaric, isothermal, and adiabatic processes.

## Slide 15: Introduction to Heat Engines
One of the primary applications of thermodynamics is to Turn heat into work.
The standard heat engine works on a cyclic process:
1) extract heat from a hot reservoir,
2) perform work, using some of the extracted heat,
3) dump unused heat into a cold reservoir (often the environment).
4) repeat over and over. We represent this process with a diagram:
A “reservoir” is a large body whose temperature doesn’t change when it absorbs or gives up heat
Wby
Hot reservoir at Th
Engine:
Qh
Cold reservoir at Tc
Qc
Energy is conserved: Qh = Qc + Wby
For heat engines we will define Qh , Qc , and Wby as positive.

## Slide 16: A Simple Heat Engine: the Stirling Cycle
Two reservoirs: Th and Tc.
Four processes: Two isotherms and two isochors
The net work during one cycle: The area of the “parallelogram”.
V
Tc
Th
Va
Vb
p
1
2
3
4

## Slide 17: Act 3
Which processes in a Stirling cycle
correspond to Qh in the heat flow diagram?
a) 1
b) 2
c) 1 and 2
d) 3
e) 3 and 4
V
Tc
Th
Va
Vb
p
1
2
3
4
Wby
Hot reservoir at Th
Engine:
Qh
Cold reservoir at Tc
Qc

## Slide 18: Solution
Which processes in a Stirling cycle
correspond to Qh in the heat flow diagram?
a) 1
b) 2
c) 1 and 2
d) 3
e) 3 and 4
Process 1 is obvious, since we’re heating the gas.
In the isothermal expansion (process 2), although the temperature is kept constant we still have to put heat in to do the work from the expansion.
V
Tc
Th
Va
Vb
p
1
2
3
4
Wby
Hot reservoir at Th
Engine:
Qh
Cold reservoir at Tc
Qc

## Slide 19: The Stirling Cycle (2)
Th
Tc
3) Isochoric
Gas temperature decreases at constant volume (piston can’t move)
gas
Qc3
Th
Tc
gas
4) Isothermal
Gas is compressed at constant Tc
W4
Qc4
Th
Tc
gas
1) Isochoric Gas temperature increases at constant volume (piston can’t move)
Qh1
Th
Tc
gas
2) Isothermal
Gas expands at constant Th
W2
Qh2
The cycle goes around like this.
We don’t describe the mechanical parts that move the gas cylinder back and forth between the reservoirs.
Notes: Do the Stirling demo here.

## Slide 20: How Does this Engine Do Work?
Look at the two isothermal processes (2 and 4) on the previous slide
Process 2: expanding gas does W2 on the piston, as it expands from Va to Vb.
Process 4: contracting gas is done W4 by the piston, as it contracts from Vb to Va.
If W2 > W4, the net work is positive.
This is true, because the contracting gas is colder (lower pressure).
During one cycle:
 The hot reservoir has lost some energy (Qh=Qh1+Qh2).
 The cold reservoir has gained some energy (Qc=Qc3+Qc4).
 The engine (the gas cylinder) has neither gained nor lost energy.
The energy to do work comes from the hot reservoir, not from the engine itself.
The net work done by the engine is:
Wby = W2 - W4 = Qh - Qc= Qh2 - Qc4
Not all of the energy taken from the hot reservoir becomes useful work. Some is lost into the cold reservoir. We would like to make Qc as small as possible.

## Slide 21: Heat Engine Efficiency
What’s the best we can do?
The Second Law will tell us.
We pay for the heat input, QH, so:
Define the efficiency
Valid for all heat engines. (Conservation of energy)
Cartoon picture of a heat engine:
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
Wby
Remember:
We define Qh and Qc as positive. The arrows define direction of flow.
Engine

## Slide 22: The 2nd Law Sets the Maximum Efficiency (1)
How to calculate Stot?
Over one cycle:
Stot = Sengine + Shot +Scold
Remember: Qh is the heat taken from the hot reservoir, so Shot = -Qh/Th.
Qc is the heat added to the cold reservoir, so Scold = +Qc/Tc.
= 0
From the definition of T
2nd Law
Qc cannot be zero. Some energy is always lost.

## Slide 23: The 2nd Law Sets the Maximum Efficiency (2)
This is a universal law !! (equivalent to the 2nd law)
It is valid for any procedure that converts thermal energy into work.
We did not assume any special properties (e.g., ideal gas) of the material in the derivation.
The maximum possible efficiency, Carnot = 1 - Tc/Th, is called the Carnot efficiency.
The statement that heat engines have a maximum efficiency was the first expression of the 2nd law, by Sadi Carnot in 1824.

## Slide 24: How Efficient Can an Engine be?
Consider an engine that uses steam (Th = 100° C) as the hot reservoir and ice (Tc = 0° C) as the cold reservoir. How efficient can this engine be?
The Carnot efficiency is
Therefore, an engine that operates between these two temperatures can, at best, turn only 27% of the steam’s heat energy into useful work.
Question: How might we design an engine that has higher efficiency?
Answer: By increasing Th. (That’s more practical than lowering Tc.)
Electrical power plants and race cars obtain better
performance by operating at a much higher Th.
Notes: Show Steam engine and thermoelectric fan here ??

## Slide 25: When Is  Less than Carnot?
Lesson: Avoid irreversible processes.
(ones that increase Stot).
 direct heat flow from hot to cold
 free expansion (far from equilibrium)
 sliding friction
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Engine
We can write the efficiency loss in terms of the change of total entropy:
Carnot

## Slide 26: Next Time
Carnot Engines Refrigerators Heat Pumps