## Slide 1: Lecture 13 Heat Engines
 Thermodynamic processes and entropy
 Thermodynamic cycles
 Extracting work from heat
- How do we define engine efficiency?
- Is there an efficiency limit?
- Stirling Cycle
Reading for this Lecture:
Elements Ch 4D-E, 10A-B
Notes: 1
DEMOS:
* Stirling (hand held) - no time for the other Stirling engine.
* Thermolectric powered fan
* Steam engine

## Slide 2: L12: Blackbody Radiation
The Planck law gives the spectrum of electromagnetic energy contained in modes with frequencies between f and f + f:
Integrating over all frequencies gives the total radiated energy per unit surface area:
The power radiated per unit surface area by a perfect radiator is:
The total power radiated = JArea
Stefan-Boltzmann Law of Radiation
SB = 5.67010-8 W m-2 K-4 Stefan-Boltzmann constant
2.8
Planck Radiation Law
hf/kT
U(f)
Just a number: 4/15

## Slide 3: Not all Bodies are Black
Modified Stefan-Boltzmann
Law of Radiation:
Typical emissivities (300 K): gold, polished 0.02 aluminum, anodized 0.55 white paper 0.68 brick 0.93 soot 0.95 skin (!) 0.98
Real materials are not truly “black” (i.e., they don’t completely absorb all wavelengths). The fraction absorbed is called absorbance, which is equal* to its emissivity, e, a dimensionless number 0  e  1 that depends on the properties of the surface.
e = 1 for an ideal emitter (an ideal blackbody absorber).
e = 0 for something that doesn’t emit (or absorb) at all, i.e., a perfect reflector.
*If this equality didn’t hold, we wouldn’t have thermal equilibrium.
Notes: Leslie Cube Demo:
Only show black [~10.1], aluminum (not anodized) [~2.8], and mirror [0.7]

## Slide 5: Application: The Earth’s Temperature
The Earth’s temperature remains approximately constant, because the thermal radiation it receives from the Sun is balanced by the thermal radiation it emits.
This works because, although the Sun is much hotter (and therefore emits much more energy), the Earth only receives a small fraction.
T
T
Note: The magnitude of the Earth curve has been magnified 500,000 times

## Slide 6
Balance the energy flow: Power absorbed from sun = Power radiated by earth  TE = 280 K (~room temperature!)
R Rs
TE
The Earth’s Temperature (2)
Ts
JS = Sun’s flux at its surface = SBTS4
JR = Sun’s flux at the Earth = SBTS4(RS/R)2
JE = Earth’s flux at its surface = SBTE4
RS = 7108 m
R = 1.51011 m TS = 5800 K
But wait! We did not account for the fact that about 30% of the sun’s radiation reflects off our atmosphere! (The planet’s “albedo”.)
30% less input from the sun means about 8% lower temperature because T  P1/4 . This factor reduces our best estimate of the Earth’s temperature by about 30 K. Now TE = 250 K, or 0° F. Brrr!
In fact the average surface temperature of the Earth is about 290 K, or about 60° F, just right for Earthly life. (coincidence? I think not.)
The extra 60° F of warming is mainly due to the “greenhouse effect”, the fact that some of the radiation from the Earth is reflected back by the atmosphere. What exactly is the “greenhouse effect”?
Notes: This is now a Discussion problem…

## Slide 7: Remember Molecular vibrations:
Polyatomic molecules (e.g., CO2, H2O, CH4) have rotational and vibrational modes that correspond to photon wavelengths (energies) in the infrared. These molecules absorb (and emit) IR radiation much more effectively than O2 and N2.
This absorption is in the middle of the Earth’s thermal spectrum, but in the tail of the Sun’s.
The result is that our atmosphere lets most of the sunlight through, but absorbs a larger fraction of the radiation that the Earth emits.
Strong absorption in the infrared. (rotational and vibrational motions)
u(f)
2.8 kTS
Planck Radiation Law (not to scale: TSun ~ 20 TEarth)
hf = photon energy
2.8 kTE
Earth
Sun
Greenhouse gas absorption (Infrared)
CO2 or H2O
Photon
 = hf

## Slide 9: Some Absorption Spectra
Peak wavelength of Earth’s thermal spectrum
Peak wavelength of Sun’s thermal spectrum
Water is the most important greenhouse gas.

## Slide 10: The Greenhouse Effect
Thermal radiation from the earth (infrared) is absorbed by certain gases in our atmosphere (such as CO2) and redirected back to earth.
These ‘greenhouse gases’ provide additional warming to our planet - essential for life as we know it.
Radiation from the sun is not affected much by the greenhouse gases because it has a much different frequency spectrum.
Mars has a thin atmosphere with few greenhouse gases: 70° F in the day and -130° F at night. Venus has lots of CO2 : T = 800° F
Earth
Sun

## Slide 11: Review Entropy in Macroscopic Systems
Traditional thermodynamic entropy: S = k ln = k
We want to calculate S from macrostate information (p, V, T, U, N, etc.) Start with the definition of temperature in terms of entropy:
The entropy changes when T changes: (We’re keeping V and N fixed.)
If CV is constant:

## Slide 13: Entropy in Quasi-static Heat Flow
When V is constant: dS  dU/T = dQ/T  W = 0, so dU = dQ
In fact, dS = dQ/T during any reversible (quasi-static) process, even if V changes.
The reason: In a reversible process, Stot (system plus environment) doesn’t change:
for any reversible process
Stot = 0 if process is reversible.
The reservoir is supplying (or absorbing) heat.
The reservoir’s energy gain is the system’s heat loss. That’s how they interact.

## Slide 14: S in Isothermal Processes
p
V
1
2
T=constant
Suppose V & p change but T doesn’t - that’s isothermal.
Work is done (dWby = pdV). Heat must enter to keep T constant: dQ = dU+dWby.
So:
Special case, ideal gas:
For an ideal gas, if dT = 0, then dU = 0.
Remember: This holds for quasi-static processes, in which the system remains near thermal equilibrium at all times.
We’ve seen this before:  = (nTV)N / N!
Notes: Why? Because number of states ~V^N

## Slide 15: ACT 1
1) The entropy of a gas increases during a quasi-static isothermal expansion. What happens to the entropy of the environment?
a) Senv < 0 b) Senv = 0 c) Senv > 0
2) Consider instead the ‘free’ expansion (i.e., not quasi-static) of a gas. What happens to the total entropy during this process?
a) Stot < 0 b) Stot = 0 c) Stot > 0
vacuum
Remove the barrier
gas

## Slide 17: Quasi-static Adiabatic Processes
Q = 0 (definition of an adiabatic process)  TdS = 0
V and T both change as the applied pressure changes.
For example, if p increases (compress the system):
 V decreases, and the associated S also decreases.  T increases, and the associated S also increases.
These two effects must exactly cancel !!
Why? Because:
 This is a reversible process, so Stot = 0.  No other entropy is changing. (Q = 0, and Wby just moves the piston.)
So, in a quasi-static adiabatic process, S = 0.
Note: We did not assume that the system is an ideal gas. This is a general result.
system
Insulated walls
p
V
1
2
TH
TC
Notes: they will show this explicitly in HW for an ideal gas

## Slide 18: Irreversible Processes
Entropy-increasing processes are irreversible,
because the reverse processes would reduce entropy, and that doesn’t happen!.
Examples:
 Free-expansion (actually, any particle flow between regions of different density)
 Heat flow between two systems with different temperatures.
Consider the four processes of interest here:
Isothermal: Heat flow but no T difference. Reversible
Adiabatic: Q = 0. No heat flow at all. Reversible
Isochoric & Isobaric: Heat flow between different T’s. Irreversible
(Assuming that there are only two reservoirs.)
reversible reversible irreversible irreversible
V
p
isotherm
adiabat
V
p
isochor
V
p
isobar
V
p

## Slide 19: Two blocks, each with heat capacity* C = 1 J/K are initially at different temperatures, T1 = 250 K, T2 = 350 K. They are then placed into contact, and eventually reach a final temperature of 300 K. (Why?) What can you say about the total change in entropy Stot? a) Stot < 0 b) Stot = 0 c) Stot > 0
ACT 2
T1
T2
Tf
Tf
T1 = 250K
T2 = 350K
Tf = 300 K
Two masses each with heat capacity C = 1J/K*
*For a solid, C = CV = Cp, to good approximation, since V  0.

## Slide 21: A Review of Some Thermodynamic Processes of an Ideal Gas
Isochoric (constant volume)
V
p
1
2
Q
Temperature changes
V
p
1
2
Q
p
Temperature and volume change
Isobaric (constant pressure)
We will assume ideal gases in our treatment of heat engines, because that simplifies the calculations.

## Slide 22
p
V
1
2
Q
Thermal Reservoir
T
Volume and pressure change
p
V
1
2
Volume, pressure and temperature change
Isothermal (constant temperature)
Review (2)
Adiabatic (no heat flow)

## Slide 23: Closed Thermodynamic Cycles
V
p
1
2
3
A closed cycle is one in which the system returns to the initial state. (same p, V, and T) For example:
 U is a state function. Therefore:
 The net work is the enclosed area.
 Energy is conserved (1st Law):
Closed cycles will form the basis of our heat engine discussion.
This is the reason that neither W nor Q is a state function. It makes no sense to talk about a state having a certain amount of W.
Though of course we could use any curves to make a closed cycle, here we will consider
isochoric, isobaric, isothermal, and adiabatic processes.

## Slide 25: Introduction to Heat Engines
One of the primary applications of thermodynamics is to Turn heat into work.
The standard heat engine works on a cyclic process:
1) extract heat from a hot reservoir,
2) perform work, using some of the extracted heat,
3) dump unused heat into a cold reservoir (often the environment).
4) repeat over and over. We represent this process with a diagram:
A “reservoir” is a large body whose temperature doesn’t change when it absorbs or gives up heat
Wby
Hot reservoir at Th
Engine:
Qh
Cold reservoir at Tc
Qc
Energy is conserved: Qh = Qc + Wby
For heat engines we will define Qh , Qc , and Wby as positive.

## Slide 26: A Simple Heat Engine: the Stirling Cycle
Two reservoirs: Th and Tc.
Four processes: Two isotherms and two isochors
The net work during one cycle: The area of the “parallelogram”.
V
Tc
Th
Va
Vb
p
1
2
3
4

## Slide 27: Act 3
Which processes in a Stirling cycle
correspond to Qh in the heat flow diagram?
a) 1
b) 2
c) 1 and 2
d) 3
e) 3 and 4
V
Tc
Th
Va
Vb
p
1
2
3
4
Wby
Hot reservoir at Th
Engine:
Qh
Cold reservoir at Tc
Qc

## Slide 29: The Stirling Cycle (2)
Th
Tc
3) Isochoric
Gas temperature decreases at constant volume (piston can’t move)
gas
Qc3
Th
Tc
gas
4) Isothermal
Gas is compressed at constant Tc
W4
Qc4
Th
Tc
gas
1) Isochoric Gas temperature increases at constant volume (piston can’t move)
Qh1
Th
Tc
gas
2) Isothermal
Gas expands at constant Th
W2
Qh2
The cycle goes around like this.
We don’t describe the mechanical parts that move the gas cylinder back and forth between the reservoirs.
Notes: Do the Stirling demo here.

## Slide 30: How Does this Engine Do Work?
Look at the two isothermal processes (2 and 4) on the previous slide
Process 2: expanding gas does W2 on the piston, as it expands from Va to Vb.
Process 4: contracting gas is done W4 by the piston, as it contracts from Vb to Va.
If W2 > W4, the net work is positive.
This is true, because the contracting gas is colder (lower pressure).
During one cycle:
 The hot reservoir has lost some energy (Qh=Qh1+Qh2).
 The cold reservoir has gained some energy (Qc=Qc3+Qc4).
 The engine (the gas cylinder) has neither gained nor lost energy.
The energy to do work comes from the hot reservoir, not from the engine itself.
The net work done by the engine is:
Wby = W2 - W4 = Qh - Qc= Qh2 - Qc4
Not all of the energy taken from the hot reservoir becomes useful work. Some is lost into the cold reservoir. We would like to make Qc as small as possible.

## Slide 31
Total work done by the gas is the sum of steps 2 and 4:
Example: Efficiency of Stirling Cycle
p
V
Tc
Th
Va
Vb
1
2
3
4
Area enclosed:
We need a temperature difference if we want to get work out of the engine.
Notes: Could possibly move to Friday lecture.

## Slide 33
Heat extracted from the hot reservoir, exhausted to cold reservoir:
Solution
p
V
Tc
Th
Va
Vb
1
2
3
4
Area enclosed:

## Slide 34
Let’s put in some numbers: Vb = 2Va  = 3/2 (monatomic gas) Th = 373K (boiling water) Tc = 273K (ice water)
For comparison: carnot = 1 – 273/373 = 26.8%
Solution
Notes: Comment: You will get the best efficiency for the largest deltaT, and for the largest “compression ratio, V2/V1.

## Slide 35: Next Time
Carnot Engines Refrigerators Heat Pumps