## Slide 1: Lecture 4: Classical Illustrations of Macroscopic Thermal Effects
 Heat capacity of solids & liquids
 Thermal conductivity
Reference for Lecture 5:
Elements Ch 5
References for this Lecture:
Elements Ch 3,4A-C
Notes: 1
Demos:
* Brass block in boiling water
Water/washer heat capacity
* Unburnable paper
* Rods in LN2

## Slide 2: Last time: Heat capacity
Remember the 1st Law of Thermodynamics:
Q = U + Wby (conservation of energy)
If we add heat to a system, it can do two things:
 Raise the temperature (internal energy increases)  Do mechanical work (e.g., expanding gas)
How much does the temperature rise?
Define heat capacity to be the amount of heat required to raise the temperature by 1 K.
The heat capacity is proportional to the amount of material.
It can be measured either at constant volume (CV) or constant pressure (CP). It depends on the material, and may also be a function of temperature.

## Slide 3: Heat Capacity of a Solid
The atoms in a solid behave like little balls connected by springs. Here’s one atom:
It has x, y, and z springs as well as x, y, and z motion.
If T is not too low, the equipartition theorem applies, and each kinetic and potential term contributes ½ kT to the internal energy:
U = 3(½ kT) + 3(½ kT) = 3kT
Therefore, a solid with N atoms has this heat capacity:
C = 3Nk = 3nR
Note: For solids (and most liquids), the volume doesn’t change much,
so CP ~ CV (no work is done).
The temperature dependence of C is usually much larger in solids and
liquids than in gases (because the forces between atoms are more important).
x
z
y
Equipartition often works near room temperature and above.
Notes: Lucite block demo – C depends on the size of the block – c divides out the mass/number of particles.

## Slide 5: Heat Capacity and Specific Heat
Heat capacity: The heat energy required to raise the temperature of an object by 1K (=1º C).
It depends on the amount of material. Units: J / K
Specific heat: The heat capacity normalized to a standard amount of material (mass or moles).
It only depends on the kind of material.
Normalize to mass: Units: J/kg.K
Normalize to moles: Units: J/mole.K “molar specific heat”
Normalize to volume: Units: J/m3.K “volume specific heat”
Question: Which has the higher c, aluminum or lead?
Upper case “C”
Lower case “c”
Notes: Answer: aluminum  a kg of Al has more atoms than a kg of lead  higher c
c_Al = 900 J/kg-K
c_Pb = 128 J/kg-K
Work dropped balls example:
Dropped (lead) balls…dropped 20 x 1 m. DeltaU=mgh = C deltaT = mc deltaT
deltaT = mgh/mc = gh/c = 9.8x20/128 = 1.53C = 2.8F (we measured ~2F – some of the thermal energy went into the plastic, sound, etc.)

## Slide 6
Act 1
An m1 = 485-gram brass block sits in boiling water (T1 = 100 C). It is taken out of the boiling water and placed in a cup containing m2 = 485 grams of ice water (T2 = 0 C). What is the final temperature, TF, of the system (i.e., when the two objects have the same T)? (cbrass = 380 J/kg.K; cwater = 4184 J/kg.K)
a. TF < 50 C b. TF = 50 C c. TF > 50 C
Notes: Brass block and boiling water demo.

## Slide 7: Home Exercises: Cooking
While cooking a turkey in a microwave oven that puts out 500 W of power, you notice that the temperature probe in the turkey shows a 1°C temperature increase every 30 seconds. If you assume that the turkey has roughly the same specific heat as water (c= 4184 J/kg-K), what is your estimate for the mass of the turkey?
You place a copper ladle of mass mL=0.15 kg (cL = 386 J/kg-K) - initially at room temperature, Troom= 20° C - into a pot containing 0.6 kg of hot cider (cc = 4184 J/kg-K), initially at 90° C. If you forget about the ladle while watching a football game on TV, roughly what is its temperature when you try to pick it up after a few minutes?
88 C = 190 F
3.6 kg

## Slide 9: Heat Conduction
Thermal energy randomly diffuses equally in all directions, like gas particles (next lecture). More energy diffuses out of a high T region than out of a low T region, implying net energy flow from HOT to COLD.
The heat current, H, depends on the gradient of temperature,
For a continuous change of T along x: H  dT / dx
For a sharp interface between hot and cold: H  T
HOT
COLD
Notes: Compare to circuits: I ~ Delta V (large difference  large current)

## Slide 10
Heat Conduction (2)
Heat current density J is the heat flow per unit area through a material. Units: Watts/m2
J = - dT / dx (- sign because heat flows toward cold)
Thermal conductivity  is the proportionality constant, a property of the material. Units: Watts/m.K
Total heat current H is the total heat flow through the material. Units: Watts
H = J.A
Hot
Cold
J is the heat flow per unit area
H is the total heat flow through the whole area
Notes: Pass around rods, ice on blocks, unburnable paper

## Slide 11: Typical Problem in Heat Conduction
Thermal resistance is defined to make the similarity to electrical current flow (Ohm’s Law) clear:
I
R
V = V1 - V2
= voltage drop
Material with thermal conductivity 
This side is at T2
Area A
This side is at T1
Thickness d
Notes: Justify R_thermal formula:
In winter, put on more (thicker) layers to stay warm.
Also, minimize surface area (sometimes by cuddling!)

## Slide 13
Exercise: Heat Loss Through Window
If it’s 22°C inside, and 0°C outside, what is the heat flow through a glass window of area 0.3 m2 and thickness 0.5 cm ?
The thermal conductivity of glass is about 1 W/m.K.

## Slide 14
ACT 2
How much heat is lost through a double-pane version of that window, with an 0.5-cm air gap? The thermal conductivity of air is about 0.03 W/(m K).
Hint: Ignore the glass, which has a much higher conductivity than air. H is limited by the high resistance air gap.
A) 20 W B) 40 W C) 1320 W d) 44,000 W

## Slide 15: Thermal conductivities ( at 300 K):
air 0.03 W/m-K
wood 0.1 W/mK
glass 1 W/m-K
aluminum 240 W/m-K
copper 400 W/m-K
How small can  be ???
Aerogel 810-5 W/m-K
What’s aerogel?

## Slide 17: Aerogel
2.5 kg brick
2 g aerogel
 = 8 x 10-5 W/m-K
An artificial substance formed by specially drying a wet silica gel, resulting in a solid mesh of microscopic strands.
Used on space missions to catch comet dust
The least dense solid material known ( = 1.9 mg/cm3. air = 1.2 mg/cm3). 98% porous, but nevertheless, quite rigid:

## Slide 18: How Long Does Heat Conduction Take?
The heat current H depends on the temperature difference between the two samples, and the thermal resistance: Rth = d/A.
Assume that all the heat leaving A enters B.
The temperature of the samples depends on their initial temperatures, the amount of heat flowing into (out of) them, and their heat capacities.
In general, the time to reach thermal equilibrium is a nontrivial problem (Friday...), but we can estimate the time it will take.
Rth

## Slide 19: How Long to Equilibrate a Rod?
The rate at which heat flows from hot to cold is about
H = AT / d.
The heat capacity is C = cm = c vol) = c  (dA) = density
So the rate at which T is reduced is about
Alternatively, the typical distance that the thermal energy has diffused varies with the square root of the time: d t . This fact is a result of the random nature of heat flow, which we’ll discuss more next lecture.
length d
Area A
T
T+T
Notes: Comparison to electric RC networks...

## Slide 21
You are cooking with two pots that have the same volume. Pot B has half the height, but twice the area as Pot A. Initially the pots are both full of boiling water (e.g., 100 C). You set them each on the bottom of your metal sink. Which cools faster?
A) Pot A
B) Pot B
C) They cool at same rate
ACT 3: Cooling pots
A
B

## Slide 22: Heat conduction – How long does it take?
Heat “into” A:
Guess solution: T(t) = T(t=0) e-t/, or TA(t) = TB + (TA0 – TB) e-t/
Plug into above DiffEQ:  = RthCA (like a discharging capacitor!)
For simplicity we assume that system B is really big (a “thermal reservoir”), so that it’s temperature is always TB.
TA(t)
TB
TA(t) = TB + T(t)
TA0
TB

## Slide 23: Act 4: Exponential Cooling
A hot steel bearing (at T = 200 C) is dropped into a large vat of cold water at 10 C. Compare the time it takes the bearing to cool from 200 to 190 C to the time it takes to cool from 100 to 90 C.(Assume the specific heat of steel is ~constant over this temperature range.)
a. t200190C > t10090C b. t200190C = t10090C c. t200190C < t10090C

## Slide 25: FYI: Thermal Diffusion and Heat Conduction
How is it that random motion can give heat flow in a particular direction?
Thermal energy randomly diffuses around, spreading out. However, the heat flow out of a region is proportional to the amount of energy that is there at that time.
Look at region 2. More heat will randomly diffuse in from a high T region than from low T: J12 > J21, and J23 > J32.
So there will be a net flow of heat in the direction of decreasing T.
In 1-D the heat current density is:
where is the thermal conductivity, a property of the material.
x
T
1 2 3
J12
J21
J23
J32

## Slide 26
Next Time
 Random Walk and Particle Diffusion
 Counting and Probability
 Microstates and Macrostates
 The meaning of equilibrium