## Slide 1: Lecture 13 Heat Engines
 Thermodynamic processes and entropy
 Thermodynamic cycles
 Extracting work from heat
- How do we define engine efficiency?
- Carnot cycle: the best possible efficiency
Reading for Lecture 14:
Elements Ch 10
Reading for this Lecture:
Elements Ch 4D-F
Notes: 1
DEMOS:
* Stirling (hand held) - no time for the other Stirling engine.
* Thermolectric powered fan
* Steam engine

## Slide 2: A Review of Some Thermodynamic Processes of an Ideal Gas
Isochoric (constant volume)
V
p
1
2
Q
Temperature changes
V
p
1
2
Q
p
Temperature and volume change
Isobaric (constant pressure)
We will assume ideal gases in our treatment of heat engines, because that simplifies the calculations.

## Slide 3
p
V
1
2
Q
Thermal Reservoir
T
Volume and pressure change
p
V
1
2
Volume, pressure and temperature change
Isothermal (constant temperature)
Review (2)
Adiabatic (no heat flow)

## Slide 5: Closed Thermodynamic Cycles
V
p
1
2
3
A closed cycle is one in which the system returns to the initial state. (same p, V, and T) For example:
 U is a state function. Therefore:
 The net work is the enclosed area.
 Energy is conserved (1st Law):
Closed cycles will form the basis of our heat engine discussion.
This is the reason that neither W nor Q is a state function. It makes no sense to talk about a state having a certain amount of W.
Though of course we could use any curves to make a closed cycle, here we will consider
isochoric, isobaric, isothermal, and adiabatic processes.

## Slide 6: Introduction to Heat Engines
One of the primary applications of thermodynamics is to Turn heat into work.
The standard heat engine works on a cyclic process:
1) extract heat from a hot reservoir,
2) perform work, using some of the extracted heat,
3) dump unused heat into a cold reservoir (often the environment).
4) repeat over and over. We represent this process with a diagram:
A “reservoir” is a large body whose temperature doesn’t change when it absorbs or gives up heat
Wby
Hot reservoir at Th
Engine:
Qh
Cold reservoir at Tc
Qc
Energy is conserved: Qh = Qc + Wby
For heat engines we will define Qh , Qc , and Wby as positive.

## Slide 7: A Simple Heat Engine: the Stirling Cycle
Two reservoirs: Th and Tc.
Four processes: Two isotherms and two isochors
The net work during one cycle: The area of the “parallelogram”.
V
Tc
Th
Va
Vb
p
1
2
3
4

## Slide 9: The Stirling Cycle (2)
Th
Tc
3) Isochoric
Gas temperature decreases at constant volume (piston can’t move)
gas
Qc3
Th
Tc
gas
4) Isothermal
Gas is compressed at constant Tc
W4
Qc4
Th
Tc
gas
1) Isochoric Gas temperature increases at constant volume (piston can’t move)
Qh1
Th
Tc
gas
2) Isothermal
Gas expands at constant Th
W2
Qh2
The cycle goes around like this.
We don’t describe the mechanical parts that move the gas cylinder back and forth between the reservoirs.
Notes: Do the Stirling demo here.

## Slide 10: How Does this Engine Do Work?
Look at the two isothermal processes (2 and 4) on the previous slide
Process 2: expanding gas does W2 on the piston, as it expands from Va to Vb.
Process 4: contracting gas is done W4 by the piston, as it contracts from Vb to Va.
If W2 > W4, the net work is positive.
This is true, because the contracting gas is colder (lower pressure).
During one cycle:
 The hot reservoir has lost some energy (Qh=Qh1+Qh2).
 The cold reservoir has gained some energy (Qc=Qc3+Qc4).
 The engine (the gas cylinder) has neither gained nor lost energy.
The energy to do work comes from the hot reservoir, not from the engine itself.
The net work done by the engine is:
Wby = W2 - W4 = Qh - Qc= Qh2 - Qc4
Not all of the energy taken from the hot reservoir becomes useful work. Some is lost into the cold reservoir. We would like to make Qc as small as possible.

## Slide 11: Act 1
On the last slide, why did we write Qh - Qc= Qh2 - Qc4?
What happened to Qh1 and Qc3? (since Qh = Qh1 + Qh2, and Qc = Qc1 + Qc2)
a) They both = 0.
b) They are not = 0, but they cancel. c) They average to zero over many cycles.

## Slide 13: Heat Engine Efficiency
What’s the best we can do?
The Second Law will tell us.
We pay for the heat input, QH, so:
Define the efficiency
Valid for all heat engines. (Conservation of energy)
Cartoon picture of a heat engine:
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
Wby
Remember:
We define Qh and Qc as positive. The arrows define direction of flow.
Engine

## Slide 14: Review Entropy in Macroscopic Systems
Traditional thermodynamic entropy: S = k ln = k
We want to calculate S from macrostate information (p, V, T, U, N, etc.) Start with the definition of temperature in terms of entropy:
The entropy changes when T changes: (We’re keeping V and N fixed.)
If CV is constant:

## Slide 15: Entropy in Quasi-static Heat Flow
When V is constant: dS  dU/T = dQ/T  W = 0, so dU = dQ
In fact, dS = dQ/T during any reversible (quasi-static) process, even if V changes.
The reason: In a reversible process, Stot (system plus environment) doesn’t change:
for any reversible process
Stot = 0 if process is reversible.
The reservoir is supplying (or absorbing) heat.
The reservoir’s energy gain is the system’s heat loss. That’s how they interact.

## Slide 17: S in Isothermal Processes
p
V
1
2
T=constant
Suppose V & p change but T doesn’t.
Work is done (dWby = pdV). Heat must enter to keep T constant: dQ = dU+dWby.
So:
Special case, ideal gas:
For an ideal gas, if dT = 0, then dU = 0.
Remember: This holds for quasi-static processes, in which the system remains near thermal equilibrium at all times.
Notes: Why? Because number of states ~V^N

## Slide 18: Quasi-static Adiabatic Processes
Q = 0 (definition of an adiabatic process)
V and T both change as the applied pressure changes.
For example, if p increases (compress the system):
 V decreases, and the associated S also decreases.  T increases, and the associated S also increases.
These two effects must exactly cancel !!
Why? Because:
 This is a reversible process, so Stot = 0.  No other entropy is changing. (Q = 0, and Wby just moves the piston.)
So, in a quasi-static adiabatic process, S = 0.
Note: We did not assume that the system is an ideal gas. This is a general result.
system
Insulated walls
p
V
1
2
TH
TC
Notes: they will show this explicitly in HW for an ideal gas

## Slide 19: Heat Engine Efficiency
What’s the best we can do?
The Second Law will tell us.
We pay for the heat input, QH, so:
Define the efficiency
Valid for all heat engines. (Conservation of energy)
Cartoon picture of a heat engine:
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
Wby
Remember:
We define Qh and Qc as positive. The arrows define direction of flow.
Engine

## Slide 21: The 2nd Law Sets the Maximum Efficiency (1)
How to calculate Stot?
Over one cycle:
Stot = Sengine + Shot +Scold
Remember: Qh is the heat taken from the hot reservoir, so Shot = -Qh/Th.
Qc is the heat added to the cold reservoir, so Scold = +Qc/Tc.
= 0
From the definition of T
2nd Law
Qc cannot be zero. Some energy is always lost.

## Slide 22: The 2nd Law Sets the Maximum Efficiency (2)
This is a universal law !! (equivalent to the 2nd law)
It is valid for any procedure that converts thermal energy into work.
We did not assume any special properties (e.g., ideal gas) of the material in the derivation.
The maximum possible efficiency, Carnot = 1 - Tc/Th, is called the Carnot efficiency.
The statement that heat engines have a maximum efficiency was the first expression of the 2nd law, by Sadi Carnot in 1824.

## Slide 23: How Efficient Can an Engine be?
Consider an engine that uses steam (Th = 100° C) as the hot reservoir and ice (Tc = 0° C) as the cold reservoir. How efficient can this engine be?
The Carnot efficiency is
Therefore, an engine that operates between these two temperatures can, at best, turn only 27% of the steam’s heat energy into useful work.
Question: How might we design an engine that has higher efficiency?
Answer: By increasing Th. (That’s more practical than lowering Tc.)
Electrical power plants and race cars obtain better
performance by operating at a much higher Th.
Notes: Show Steam engine and thermoelectric fan here ??

## Slide 25: When Is  Less than Carnot?
Lesson: Avoid irreversible processes.
(ones that increase Stot).
 direct heat flow from hot to cold
 free expansion (far from equilibrium)
 sliding friction
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Engine
We can write the efficiency loss in terms of the change of total entropy:
Carnot

## Slide 26: Irreversible Processes
Entropy-increasing processes are irreversible,
because the reverse processes would reduce entropy.
Examples:
 Free-expansion (actually, any particle flow between regions of different density)
 Heat flow between two systems with different temperatures.
Consider the four processes of interest here:
Isothermal: Heat flow but no T difference. Reversible
Adiabatic: Q = 0. No heat flow at all. Reversible
Isochoric & Isobaric: Heat flow between different T’s. Irreversible
(Assuming that there are only two reservoirs.)
reversible reversible irreversible irreversible
V
p
isotherm
adiabat
V
p
isochor
V
p
isobar
V
p

## Slide 27: Act 2: Stirling Efficiency
Will our Stirling engine achieve Carnot efficiency?
a) Yes b) No
V
Tc
Th
Va
Vb
p
1
2
3
4

## Slide 29: How to Achieve Carnot Efficiency
V
Tc
Th
Vb Va Vc Vd
p
1
2
3
4
To achieve Carnot efficiency, we must replace the isochors (irreversible) with reversible processes. Let’s use adiabatic processes, as shown:
Processes 1 and 3 are now adiabatic.
Processes 2 and 4 are still isothermal.
This cycle is reversible, which means: Stot remains constant:   = Carnot.
This thermal cycle is called the Carnot cycle,
and an engine that implements it is called a
Carnot heat engine.
Notes: http://galileoandeinstein.physics.virginia.edu/more_stuff/flashlets/carnot.htm

## Slide 30
Total work done by the gas is the sum of steps 2 and 4:
Example: Efficiency of Stirling Cycle
p
V
Tc
Th
Va
Vb
1
2
3
4
Area enclosed:
We need a temperature difference if we want to get work out of the engine.
Notes: Could possibly move to Friday lecture.

## Slide 31
Heat extracted from the hot reservoir, exhausted to cold reservoir:
Solution
p
V
Tc
Th
Va
Vb
1
2
3
4
Area enclosed:

## Slide 33
Let’s put in some numbers: Vb = 2Va  = 3/2 (monatomic gas) Th = 373K (boiling water) Tc = 273K (ice water)
For comparison: carnot = 1 – 273/373 = 26.8%
Solution
Notes: Comment: You will get the best efficiency for the largest deltaT, and for the largest “compression ratio, V2/V1.

## Slide 34: Heat Engine Summary
For all cycles:
For the Carnot cycle:
Carnot (best) efficiency:
Carnot engines are an idealization - impossible to realize. They require very slow processes, and perfect insulation. When there’s a net entropy increase, the efficiency is reduced:
Some energy is dumped into the cold reservoir.
Qc cannot be reduced to zero.
Only for reversible cycles.

## Slide 35: Next Time
Heat Pumps Refrigerators, Available Work and Free Energy