## Slide 1: Lecture 14 Carnot engines, Refrigerators and Heat Pumps
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Heat pump
Heat leak
b
a
p
pb
pa
V
V1 V2
c
d
adiabats
Reading for this Lecture:
Elements Ch 4E-F, 10A-B
Notes: DEMOS:
* Stirling engine driven by hot washer and ice.
* Peltier cooler.

## Slide 2: Heat Engine Efficiency
What’s the best we can do?
The Second Law will tell us.
We pay for the heat input, QH, so:
Define the efficiency
Valid for all heat engines. (Conservation of energy)
Cartoon picture of a heat engine:
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
Wby
Remember:
We define Qh and Qc as positive. The arrows define direction of flow.
Engine

## Slide 3: Heat Engine Summary
For all cycles:
For the Carnot cycle:
Carnot (best) efficiency:
Carnot engines are an idealization - impossible to realize. They require very slow processes, and perfect insulation. When there’s a net entropy increase, the efficiency is reduced:
Some energy is dumped into the cold reservoir.
Qc cannot be reduced to zero.
Only for reversible cycles.

## Slide 5: Act 1: Stirling Efficiency
Will our Stirling engine achieve Carnot efficiency?
a) Yes b) No
V
Tc
Th
Va
Vb
p
1
2
3
4

## Slide 6
Total work done by the gas is the sum of steps 2 and 4:
Example: Efficiency of Stirling Cycle
p
V
Tc
Th
Va
Vb
1
2
3
4
Area enclosed:
We need a temperature difference if we want to get work out of the engine.
Notes: Could possibly move to Friday lecture.

## Slide 7
Heat extracted from the hot reservoir, exhausted to cold reservoir:
Solution
p
V
Tc
Th
Va
Vb
1
2
3
4
Area enclosed:

## Slide 9
Let’s put in some numbers: Vb = 2Va  = 3/2 (monatomic gas) Th = 373K (boiling water) Tc = 273K (ice water)
For comparison: carnot = 1 – 273/373 = 26.8%
Solution
Notes: Comment: You will get the best efficiency for the largest deltaT, and for the largest “compression ratio, V2/V1.

## Slide 10: Example: Gasoline Engine
p
pb
pa
V
V1 V2
Combustion
exhaust / intake
adiabats
b
a
c
d
bc and da are nearly adiabatic processes, because the pistons move too quickly for much heat to flow.
It’s not really a heat engine because the input energy is via fuel injected directly into the engine, not via heat flow. There is no obvious hot reservoir. However, one can still calculate work and energy input for particular gas types.
We can treat the gasoline engine as an Otto cycle:

## Slide 11: Solution
b
a
p
pb
pa
V
V1 V2
c
d
adiabats
Calculate the efficiency:

## Slide 13: Solution
Compression ratio  V2/V1  10  = 1.4 (diatomic gas)  = 60%
(in reality about 30%, due to friction etc.)
b
a
p
pb
pa
V
V1 V2
c
d
adiabats
Write it in terms of volume instead of temperature. We know the volume of the cylinders.
Notes: Why not simply use a higher compression ratio?
  V2 big  huge, heavy engine
  V1 small  temp. gets too high  premature ignition  need to use octane in gas to raise combustion temperature
  In a diesel engine, the combustion is intented to be *caused* by the compression.

## Slide 14: Solution
Why not simply use a higher compression ratio?
 If V2 big, we need a huge, heavy engine (OK for fixed installations).
 If V1 small, the temperature gets too high, causing premature ignition. High compression engines need high octane gas, which has a higher combustion temperature.

## Slide 15: How to Achieve Carnot Efficiency
V
Tc
Th
Vb Va Vc Vd
p
1
2
3
4
To achieve Carnot efficiency, we must replace the isochors (irreversible) with reversible processes. Let’s use adiabatic processes, as shown:
Processes 1 and 3 are now adiabatic.
Processes 2 and 4 are still isothermal.
This cycle is reversible, which means: Stot remains constant:   = Carnot.
This thermal cycle is called the Carnot cycle,
and an engine that implements it is called a
Carnot heat engine.
Notes: http://galileoandeinstein.physics.virginia.edu/more_stuff/flashlets/carnot.htm

## Slide 17: Run the Engine in Reverse
The Carnot cycle is reversible (each step is reversible):
When the engine runs in reverse:
Heat is transferred from cold to hot by action of work on the engine. Note that heat never flows spontaneously from cold to hot; the cold gas is being heated by adiabatic compression (process 3).
Qc / Qh = Tc / Th is still true. (Note: Qh, Qc, and W are still positive!)
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Engine
V
Tc
Th
Vb Va Vc Vd
p
1
2
3
4
Reverse all the arrows
Qh
Qc

## Slide 18: Refrigerators and Heat Pumps
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Engine
Refrigerators and heat pumps are heat engines running in reverse.
How do we measure their performance? It depends on what you want to accomplish.
Refrigerator: We want to keep the food cold (Qc). We pay for W (the electric motor in the fridge).
So, the coefficient of performance, K is:
Heat pump: We want to keep the house warm (Qh). We pay for W (the electric motor in the garden).
The coefficient of performance, K is:
It’s not called “efficiency”.

## Slide 19: Helpful Hints in Dealing with Engines and Fridges
Sketch the process (see figures below). Define Qh and Qc and Wby (or Won) as positive and show directions of flow.
Determine which Q is given.
Write the First Law of Thermodynamics (FLT).
We considered three configurations of Carnot cycles:
Qh
Wby
Th
Tc
Qc
Engine: We pay for Qh, we want Wby.
Wby = Qh - Qc = Qh
Carnot:  = 1 - Tc/Th
Qleak= QC
Qh
Won
Th
Tc
Qc
Refrigerator: We pay for Won, we want Qc.
Qc = Qh - Won = Won
Carnot:  = Tc/(Th - Tc)
Qleak= Qh
Qh
Won
Th
Tc
Qc
Heat pump: We pay for Won, we want Qh.
Qh = Qc + Won = Won
Carnot:  = Th/(Th - Tc)
These both have large  when Th - Tc is small.
This has large  when Th - Tc is large.

## Slide 21
There is a 70 W heat leak (the insulation is not perfect) from a room at temperature 22°C into an ideal refrigerator. How much electrical power is needed to keep the refrigerator at -10° C? Assume Carnot performance.
Act 2: Refrigerator
a) < 70 W
b) = 70 W
c) > 70 W

## Slide 22
Supplement: Peltier cooler
Driving a current (~amps) through generates a temperature difference. 20-50˚C typical
Not so common – they’re more costly, take a lot of power, and you still have to get rid of the heat! But....no moving parts to break.
How’s it work…
Electrons pushed from electron-deficit material (p-type) to electron-rich material (n-type); they slow down, cooling the top connector. Similarly, they heat up in going from n to p-type (bottom connector).
Despite the radically different construction, this heat pump must obey exactly the same limits on efficiency as the gas-based pumps, because these limits are based on the 1st and 2nd laws, not any details.

## Slide 23
Refrigerators work less well as Th - Tc becomes large.
The colder you try to go, the less efficient the refrigerator gets. The limit as TC goes to zero is zero efficiency !
Since heat leaks will not disappear as the object is cooled, you need to supply more work the colder it gets. The integral of the power required diverges as Tc  0.
Therefore you cannot cool a system to absolute zero.
The Limits of Cooling
The maximum efficiency is
Notes: Show Peltier cooler: a non-mechanical refrigerator.

## Slide 25
Suppose that the heat flow out of your 20° C home in the winter is 7 kW. If the temperature outside is -15° C, how much power would an ideal heat pump require to maintain a constant inside temperature?
Act 3: Heat Pump
Hot reservoir at Th
Cold reservoir at Tc
Qh
Qc
W
Heat pump
Heat leak
a) W < 7 kW
b) W = 7 kW
c) W > 7 kW

## Slide 26: Next Time
Available Work and Free Energy