## Slide 1
c

I
I0
y
Sum
2I0


I
I0
Sum
2I0

c

I
I0
Sum
2I0

c/3
y
y
Lecture 5: Applications of Interference and Diffraction
Notes: Demos:
752. Laser with round pinhole, pair of round pinholes on TV
501 Michelson
162 Laser with slits
1242 Remote control (to show rectangular aperture)
Adjustable iris
??70 Soap bubble??

## Slide 2
Today
Circular Diffraction
  Angular resolution (Rayleigh’s criterion)
  Minimum spot size
Interferometers
  Michelson
  Applications

## Slide 3
The size of the spot is determined by the diameter, D, of the aperture, and wavelength, , of the incident light.
Diffraction by a circular aperture is similar to single-slit diffraction. But note the difference:
Image plane


I
I0

o

D
Image plane
Point object
Slit
Circular aperture
The “Airy disk”. The central lobe contains 84% of power.
Diffraction-limited Optics
Diffraction has important implications for optical instruments
Even for perfectly designed optics the image of a point source will be a little blurry - the circular aperture produces diffraction.
Notes: “Airy disk” after Sir George Airy. He also explained rainbows.

## Slide 4: Slits and circular apertures
Monochromatic light source at a great distance, or a laser.
Object at any distance:
Slit, width a
Lens, diameter D
Pinhole, diameter D

-/a 0 a
0
I
I0

-1.22/D 0 1.22/D
0
I
I0
Observation screen:
Image Plane:
Observation screen:
The focusing effect of the lens is independent of the diffraction effect due to the aperture
Notes: Laser with pinholes
Laser with adjustable iris (from PGK)

## Slide 5: Exercise: Expansion of a Laser beam
D
d
In 1985, a laser beam with a wavelength of  = 500 nm was fired from the earth and reflected off the space shuttle Discovery, in orbit at a distance of L = 350 km away from the laser.
If the circular aperture of the laser was D = 4.7 cm, what was the beam diameter d at the space shuttle?
Notes: Answer = 9.1 m

## Slide 6: Solution
D
d
Half-angle-width of diffraction maximum:
In 1985, a laser beam with a wavelength of  = 500 nm was fired from the earth and reflected off the space shuttle Discovery, in orbit at a distance of L = 350 km away from the laser.
If the circular aperture of the laser was D = 4.7 cm, what was the beam diameter d at the space shuttle?

## Slide 7: Act 1
D
d
To make a smaller spot on the shuttle, what should we do to the beam diameter at the source?
a. reduce it b. increase it c. cannot be made smaller
In 1985, a laser beam with a wavelength of  = 500 nm was fired from the earth and reflected off the space shuttle Discovery, in orbit at a distance of L = 350 km away from the laser.

## Slide 8: Solution
D
d
To make a smaller spot on the shuttle, what should we do to the beam diameter at the source?
a. reduce it b. increase it c. cannot be made smaller
Counter-intuitive as this is, it is correct – you reduce beam divergence by using a bigger beam. (Note: this will work as long as D < d.)
We’ll see that this can be understood as a non-quantum
version of the uncertainty principle: x px>.
In 1985, a laser beam with a wavelength of  = 500 nm was fired from the earth and reflected off the space shuttle Discovery, in orbit at a distance of L = 350 km away from the laser.

## Slide 9: Exercise: Focusing a laser beam
Dlaser
d
Dlens
f
There are many times you would like to focus a laser beam to as small a spot as possible. However, diffraction limits this.
The circular aperture of a laser ( = 780 nm) has Dlaser = 5 mm. What is the spot-size d of the beam after passing through a perfect lens with focal length f = 5mm and diameter Dlens = 6 mm?
Notes: Treat the lens as two parts:
Aperture
Optics

## Slide 10: Solution
Dlaser
d
Dlens
f
The angular spread of the beam is determined by the smaller of Dlaser and Dlens. Here, it’s Dlaser.
Light at this angle will intercept the focal plane at d/2 ~ f 
There are many times you would like to focus a laser beam to as small a spot as possible. However, diffraction limits this.
The circular aperture of a laser ( = 780 nm) has Dlaser = 5 mm. What is the spot-size d of the beam after passing through a perfect lens with focal length f = 5mm and diameter Dlens = 6 mm?

## Slide 11: Act 2
 = 780 nm, Dlaser = 5 mm, f = 5 mm, Dlens = 6 mm. Which of the following will reduce the spot size?
a. increase b. decrease c. increase Dlens d. decrease Dlens
Dlaser
d
Dlens
f
(See lecture 4, exercise 2)
There are many times you would like to focus a laser beam to as small a spot as possible. However, diffraction limits this.

## Slide 12: Solution
 = 780 nm, Dlaser = 5 mm, f = 5 mm, Dlens = 6 mm. Which of the following will reduce the spot size?
a. increase b. decrease c. increase Dlens d. decrease Dlens
Dlaser
d
Dlens
f
(See lecture 4, exercise 2)
The diffraction is already limited by Dlaser. Increasing Dlens doesn’t help.
There is a huge industry devoted to developing cheap blue diode lasers ( ~ 400 nm) for just this purpose, i.e., to increase DVD capacity.
“Blue-Ray” technology!
There are many times you would like to focus a laser beam to as small a spot as possible. However, diffraction limits this.

## Slide 14
=2c

I
I0
y
Sum
2I0

Two images
resolvable
Sum
2I0

y

I
I0
=c
‘Diffraction limit’
of resolution

I
I0
=c/3
Sum
2I0

y
Two images
not resolvable
D


Two point
sources
Rayleigh’s Criterion
defines the images to be resolved if the central maximum of one image falls on or further than the first minimum of the second image.
NOTE: No interference!! Why not?
Angular Resolution
Diffraction also limits our ability to “resolve” (i.e., distinguish) two point sources. Consider two point sources (e.g., stars) with angular separation  viewed through a circular aperture or lens of diameter D.
Notes: NOTE: No interference between the two images.
Movies:
Rayd, rayw
Webtop.msstate.edu/top/movies/frau/rayd.mov
Webtop.msstate.edu/top/movies/frau/rayw.mov
DEMOS:
* 2 apertures

## Slide 15: FYI:Coherent and Incoherent Waves
We only observe interference when the sources have a definite
(usually constant) phase difference. In this case, the sources
are said to be coherent.
Examples of coherent sources:
Sound waves from speakers driven by electrical signals that have the same frequency and a definite phase.
Laser light. In a laser, all the atoms emit light with the same frequency and phase. This is a quantum effect that we’ll study later in the course.
Laser
Incoherent waves: The phase relation is random.
Waves from two unrelated sources.
Examples: light from two points on the sun or two atoms on a light bulb filament, or two people singing the same note.
Incoherent intensities add. The average of constructive and destructive interference is no interference!
The laser light is also all going the same direction.
Notes: Very fast here...
Demo: Two speakers in classroom – drive in phase
Alternative – have incoherent static from each speaker
Discuss other examples of coherence – incoherence
One music instrument – sound reflected from walls
Two instruments in tune - out of tune
Orchestra – in tune - out of tune

## Slide 16
1. Assuming diffraction-limited optics, what is the minimum angular separation of two stars that can be resolved by a D = 5 m telescope using light of  = 500 nm?
a. 0.1 rad b. 1 rad c. 10 rad
Halley’s Comet
2. If the two point sources are not quite resolved at screen 1, will they be resolved at screen 2?
a. Yes b. No
screen 1
screen 2
Act 3: Resolving Stars

## Slide 17: Solution
1. Assuming diffraction-limited optics, what is the minimum angular separation of two stars that can be resolved by a D = 5 m telescope using light of  = 500 nm?
a. 0.1 rad b. 1 rad c. 10 rad
Halley’s Comet
2. If the two point sources are not quite resolved at screen 1, will they be resolved at screen 2?
a. Yes b. No
screen 1
screen 2

## Slide 18: Solution
1. Assuming diffraction-limited optics, what is the minimum angular separation of two stars that can be resolved by a D = 5 m telescope using light of  = 500 nm?
a. 0.1 rad b. 1 rad c. 10 rad
Halley’s Comet
2. If the two point sources are not quite resolved at screen 1, will they be resolved at screen 2?
a. Yes b. No
screen 1
screen 2
c only depends on  and D. The centers of the spots are farther apart, but the spots are also wider by the same amount.

## Slide 19
Digital cameras look something like this:
If the distance between adjacent pixels is less than the minimum resolvable separation due to diffraction, then diffraction limits the image quality.
The “f-number” of a lens is defined as f/D. To minimize diffraction, you want a small f-number, i.e., a large aperture*.
d
Photosensor:
7 mm
5 mm
Pixel
*This assumes a ‘perfect lens’. In practice, lens aberrations limit the resolution if D is too big.
Photosensor
lens
Focal length f = 10 mm
Aperture, D = 3 mm
Example: Camera resolution (Next week’s discussion)
Notes: www.cambridgeincolour.com/tutorials/diffraction-photography.htm#
f/# = ‘f-number’ = f/D
“speed” of a lens  bigger collection aperature  take photo faster (in less time)

## Slide 20
Optical Interferometers
Interference arises whenever there are two (or more) ways for something to happen, e.g., two slits for the light to get from the source to the screen.
I = 4I1cos2(/2), with  = 2, and path-length difference 
An interferometer is a device using mirrors and “beam splitters” (half of the light is transmitted, half is reflected) to give two separate paths from source to detector.
Two common types:
Mach-Zehnder: Michelson :
beam-splitter
mirror
beam splitter
mirrors
mirror
beam splitter

## Slide 21
Michelson Interferometer
The Michelson interferometer works by varying the phase difference between the two paths the light can take.
One possibility is to vary the lengths L1 or L2.
This makes possible very accurate measurements of displacements.
beam
splitter
4I1
mirror
2I1
2I1
2I1
2I1
Total path length L2
Path-length difference  = L2 - L1
I = 4I1 cos2(/2), with  = 2
I1
I1
Total path length L1
mirror
Source
Be careful !!
What’s important is the total time to get back to the beam splitter...
Notes: The center of the pattern is the important spot (Why?)
501 Michelson demo.

## Slide 22: ACT 4
Consider the following Michelson interferometer. Suppose that for the setup shown, all the light (with  = 500 nm) comes out the bottom port.
1. How much does the top mirror need to be moved so that none of the light comes out the bottom port?
a. 125 nm b. 250 nm c. 500 nm
d
2. Where does the light then go?
a. down b. up c. left d. right

## Slide 23: Solution
Consider the following Michelson interferometer. Suppose that for the setup shown, all the light (with  = 500 nm) comes out the bottom port.
1. How much does the top mirror need to be moved so that none of the light comes out the bottom port?
a. 125 nm b. 250 nm c. 500 nm
d
2. Where does the light then go?
a. down b. up c. left d. right
We need to go from complete constructive to complete destructive interference  Δ = 180˚   = 
However…when we move the mirror by d, we change  by 2d.
Therefore, d = /2 = /4 = 500/4 = 125 nm.

## Slide 24: Solution
Consider the following Michelson interferometer. Suppose that for the setup shown, all the light (with  = 500 nm) comes out the bottom port.
1. How much does the top mirror need to be moved so that none of the light comes out the bottom port?
a. 125 nm b. 250 nm c. 500 nm
d
2. Where does the light then go?
a. down b. up c. left d. right
We need to go from complete constructive to complete destructive interference  Δ = 180˚   = 
However…when we move the mirror by d, we change  by 2d.
Therefore, d = /2 = /4 = 500/4 = 125 nm.
The light goes out the way it came in. Energy is conserved --the light can’t just disappear!
The Michelson interferometer is perhaps most famous for disproving the hypothesis that EM waves propagate through an “aether” – this result helped stimulate the Special Theory of Relativity

## Slide 25
Michelson Interferometer
Another possibility is to vary the phase by changing the speed of the waves in the two arms.
Recall v=c/n where n = index of refraction.
Using  = v/f, the number of wavelengths in arm 1 is:
and similarly for arm 2.
(You can think of it as the path being longer by n.)
The phase difference is thus:
 = 2(N1 – N2) = 2(fL/c)(n1 – n2)
This makes possible very accurate measurement of changes in the speed of light in the two arms.
mirror
beam-
splitter
Notes: A homework problem.
DEMO with pump.

## Slide 26
FYI: Application Optical Coherence Tomography
One “mirror” of the Michelson is replaced by human tissue. The type of tissue controls the amount of reflection and the phase shift.
By sending in many colors, one can learn about the density, composition, and structure of the tissue.
Used for medical diagnostics – like a microscope, but you don’t have to excise the sample from the body!
Used to study
  skin cancer
  cardiovascular disease (detect bad plaques)
  glaucoma and macular degeneration (incurable eye disease)

## Slide 27
FYI: Gravitational Wave Detection
General relativity predicts that when massive objects accelerate, they produce time-dependent gravitational fields – gravitational waves – that propagate as “warpings” of spacetime at the speed of light. (similar to EM radiation from accelerated charge)
The effect is very tiny: E.g., estimated L/L of ~10-21 for in-spiraling binary neutron stars. How to detect this???
Notes: http://sciencebulletins.amnh.org/astro/f/gravity.20041101/essays/45_2.php

## Slide 28
FYI: Application: Gravity Wave Detection
LIGO:
Laser
Interferometric
Gravitational wave
Observatory
-World’s largest interferometers: 4-km
-2 in Hanford, WA; 1 in Livingston, LO
- >500 scientists
-Achieved sensitivity L/L ~ 10-23  L ~ 10-20 m
-Six data runs completed.
-“Advanced LIGO” should improve sensitivity by another 10x.
Notes: http://sciencebulletins.amnh.org/astro/f/gravity.20041101/essays/45_2.php

## Slide 29
Consider the following “Sagnac” [“sahn-yack”] interferometer. Here the two possible paths are the clockwise and counter-clockwise circuits around the fiber loop.
2. How could we change the relative path-length difference, and thereby change how much light exits the bottom port?
1. If we insert an extra piece of glass as shown, how does the relative path length change?
fiber loop
FYI: Modern Applications in Navigation

## Slide 30
Consider the following “Sagnac” [“sahn-yack”] interferometer. Here the two possible paths are the clockwise and counter-clockwise circuits around the fiber loop.
  It doesn’t! Because the interference paths completely overlap, the Sagnac is a remarkably stable interferometer, e.g., to temperature fluctuations in the fiber.
2. How could we change the relative path-length difference, and thereby change how much light exits the bottom port?
1. If we insert an extra piece of glass as shown, how does the relative path length change?
fiber loop
FYI: Modern Applications in Navigation

## Slide 31: FYI: Modern Applications in Navigation
Consider the following “Sagnac” [“sahn-yack”] interferometer. Here the two possible paths are the clockwise and counter-clockwise circuits around the fiber loop.
  It doesn’t! Because the interference paths completely overlap, the Sagnac is a remarkably stable interferometer, e.g., to temperature fluctuations in the fiber.
2. How could we change the relative path-length difference, and thereby change how much light exits the bottom port?
  Rotate the entire interferometer (in the plane of the paper). For example, if we rotate it clockwise, the light making the clockwise circuit will have farther to go (the beamsplitter is “running away”), while the counterclockwise path will be shortened.
  It is not difficult to show that
1. If we insert an extra piece of glass as shown, how does the relative path length change?
fiber loop
  Monitor output intensity  determine   rate of rotation   “laser ring gyroscope”!

## Slide 32
Next Week
Introduction to quantum mechanics Photoelectric effect Relation between energy and frequency of a photon Photon momentum The key relations of quantum mechanics Wave-particle duality