## Slide 1
Lecture 4: Diffraction & Spectroscopy
y
L
d

Spectra of atoms reveal the quantum nature of matter
Take a plastic grating from the bin as you enter class.
Notes: You MUST at least get through the calculation of the minima in single-slit diffraction, in order for the students to understand the lab and the discussion this week!
Tell the students to take gratings as they enter.
DEMOS:
* ---- Computer “slits” program
* 162 Laser with multiple slits slides.
* 74 Xmas tree and diffraction grating handouts
* 1237 CD to show diffraction
* 1044 Green and Red lasers to shine thru diff grating
* 731 Iridescent butterfly
* 320 Phasor wheel

## Slide 2: Today’s Topics
* Derivations in Appendix (also in Young and Freeman, 36.2 and 36.4)
Single-Slit Diffraction*
Multiple-slit Interference*
Diffraction Gratings
  Spectral Resolution
Optical Spectroscopy
Interference + Diffraction

## Slide 3: Review of 2-Slit Interference
Only the phase difference matters. Phase difference is due to source phases and/or path difference.
In a more complicated geometry (see figure on right), one must calculate the total path from source to screen.
If the amplitudes are equal  Use trig identity: A = 2A1cos(/2).
Phasors: Phasors are amplitudes. Intensity is the square of the phasor length.

## Slide 4: Multiple Slit Interference
The positions of the principal maxima occur at  = 0, 2, 4, ... where  is the phase between adjacent slits.  = 0, /d, 2/d, ...
The intensity at the peak of a principal maximum goes as N2. 3 slits: Atot = 3A1  Itot = 9I1. N slits: IN = N2I1.
Between two principal maxima there are N-1 zeros and N-2 secondary maxima  The peak width  1/N.
The total power in a principal maximum is proportional to N2(1/N) = N.



I4

16I1
N=4



I5

25I1
N=5



I3

9I1
N=3
d  d




d  d
d  d


Notes: Multi-slit computer program.

## Slide 5: N-Slit Interference
The Intensity for N equally spaced slits is given by:
Derivation (using phasors) is in the supplementary slides.
*
* Your calculator can probably graph this. Give it a try.
y
L
d

 is the phase difference between adjacent slits.
You will not be able to use the small angle approximations unless d >> 
As usual, to determine the pattern at the screen, we need to relate  to  or y = L tan:
Notes: Can show basic idea with UEK slit program

## Slide 6
Example Problem
0 min /d
In an N-slit interference pattern, at what angle min does the intensity first go to zero? (In terms of , d and N).
Notes: 162 Laser with multiple slits

## Slide 7
Solution
0 min /d
In an N-slit interference pattern, at what angle min does the intensity first go to zero? (In terms of , d and N).
But min = 2(d sinmin)/  2d min/ = 2/N. Therefore, min  /Nd.
As the number of illuminated slits increases, the peak widths decrease!
General feature: Wider slit features  narrower patterns
Narrower slit features  wider patterns....
has a zero when the numerator is zero. That is, min = 2/N.
Exception: When the denominator is also zero. That’s why there are only N-1 zeros.
Notes: 320 Phasor wheel
162 Laser slits Demo 10 slits

## Slide 8
Q: What happens when a plane wave meets a small aperture?
A: The result depends on the ratio of the wavelength  to the size of the aperture, a:
Huygens’ principle
A Consequence of Superposition
 >> a
Similar to a wave from a point source.
This effect is called diffraction.
 << a
The transmitted wave is concentrated in the forward direction, and at near distances the wave fronts have the shape of the aperture. The wave eventually spreads out.
We will next study what happens when waves pass through one slit. We will use Huygens’ principle (1678):
All points on a wave front (e.g., crest or trough) can be treated as point sources of secondary waves with speed, frequency, and phase equal to the initial wave.
Wavefront at t=0
Wavefront at later time
Notes: Do it quickly … maybe not at all.

## Slide 9
So far in the multiple-slit interference problems we have assumed that each slit is a point source.
Point sources radiate equally in all directions.
Real slits have a non-zero extent – - a “slit width” a. The transmission pattern depends on the ratio of a to .
In general, the smaller the slit width, the more the wave will diffract.
screen
Diffraction profile
I1
Large slit:
Single-slit Diffraction
screen
Diffraction profile
I1
Small slit:
Notes: 162 laser and single slit

## Slide 10: Single-Slit Diffraction
Slit of width a. Where are the minima?
Use Huygens’ principle: treat each point across the opening of the slit as a wave source.
The first minimum is at an angle such that the light from the top and the middle of the slit destructively interfere.
This works, because for every point in the top half, there is a corresponding point in the bottom half that cancels it.

a/2

P
Incident Wave
(wavelength )
y
L
a

The second minimum is at an angle such that the light from the top and a point at a/4 destructively interfere:
Location of nth-minimum:
Notes: You MUST at least get this far, in order for the students to understand the lab and the discussion this week!

## Slide 11: ACT 1
Which of the following would broaden the diffraction peak?
a. reduce the laser wavelength
b. reduce the slit width
c. move the screen further away
d. a. and b.
e. b. and c.
2 m
a
1 cm = W

## Slide 12: ACT 1 - Solution
Which of the following would broaden the diffraction peak?
a. reduce the laser wavelength
b. reduce the slit width
c. move the screen further away
d. a. and b.
e. b. and c.
2 m
a
1 cm = W

## Slide 13
Laboratory 1: Interference
In this week’s lab you will combine:
Two slits:
Multi-slit Interference I = 4I1cos2(/2) For point sources, I1 = constant.
and
Single-slit Diffraction I1()
For finite sources, I1 = I1().
to obtain
The total pattern, I = 4I1()cos2(/2)
Don’t forget … The prelab is due at the beginning of lab !!

## Slide 14: Single-slit Diffraction — Summary
The intensity of a single slit has the following form:
Single Slit Diffraction Features:
First zero:  = 2   /a
Secondary maxima are quite small.


aa

I
I0
 = phase difference between waves coming from the top and bottom of the slit.
Derivation is in the supplement.
Observer (far away)
a = a sin  a
L >> a
P

a

## Slide 15
Multi-Slit Interference + Diffraction
Combine:
Multi-slit Interference,
and
Single-slit Diffraction,
to obtain
Total Interference Pattern,
Remember:  = (d sin)/  d/a = (a sin)/  a 
 = phase between adjacent slits  = phase across one slit
You will explore these concepts in lab this week.

## Slide 16: Note:The simple calculations we have done only hold in the “far-field” (a.k.a. “Fraunhofer” limit), where L >> d2/. Intermediate cases (“Fresnel diffraction”) can be much more complex…

## Slide 17
Interference Gratings
Examples around us.
CD disk – grooves spaced by ~wavelength of visible light.
The color of some butterfly wings!
The material in the wing in not pigmented! The color comes from interference of the reflected light from the pattern of scales on the wing– a grating with spacing of order the wavelength of visible light! (See the text Young & Freeman, 36.5)
Notes: 1237 CD demo
731 Butterfly

## Slide 18
Optical spectroscopy: a major window on the world
Some foreshadowing:
Quantum mechanics  discrete energy levels, e.g., of electrons in atoms or molecules.
When an atom transitions between energy levels it emits light of a very particular frequency.
Every substance has its own signature of what colors it can emit.
By measuring the colors, we can determine the substance, as well as things about its surroundings (e.g., temperature, magnetic fields), whether its moving (via the Doppler effect), etc.
Optical spectroscopy is invaluable in materials research, engineering, chemistry, biology, medicine…
But how do we precisely measure wavelengths?
Notes: To save time in L4, Slides 13-15 should be deferred to Lecture 5.

## Slide 19: Spectroscopy Demonstration
We have set up some discharge tubes with various gases. Notice that the colors of the various discharges are quite different. In fact the light emitted from the highly excited gases is composed of many “discrete wavelengths.” You can see this with the plastic “grating” we supplied.
Your eye
Hold grating less than 1 inch from your eye.
Light source
Your view through the grating:
Put light source at left side of grating.
View spectral lines by looking at about 45o. If you don’t see anything, rotate grating 90o.
Notes: 74 Xmas tree and handouts

## Slide 20: Atomic Spectroscopy
Figure showing examples of atomic spectra for H, Hg, and Ne.
Can you see these lines in the demonstration?
You can keep the grating. See if you can see the atomic
lines in Hg or Na street lights or neon signs.
Source for figure: http://www.physics.uc.edu/~sitko/CollegePhysicsIII/28-AtomicPhysics/AtomicPhysics.htm
The lines are explained by Quantum Mechanics.

## Slide 21
The slit/line spacing determines the location of the peaks (and the angular dispersing power  of the grating:
The positions of the principal interference maxima are the same for any number of slits!
The number of slits/beam size determines the width of the peaks (narrower peaks easier to resolve).
  /Nd
Resolving power of an N-slit grating: The Rayleigh criterion
Diffraction from gratings
d sin = m

## Slide 22
Diffraction Grating Example
Angular splitting of the Sodium doublet:
Consider the two closely spaced spectral (yellow) lines of sodium (Na), 1 = 589 nm and 2 = 589.6 nm. If light from a sodium lamp fully illuminates a diffraction grating with 4000 slits/cm, what is the angular separation of these two lines in the second-order (m=2) spectrum?
Hint: First find the slit spacing d from the number of slits per centimeter.

## Slide 23
Small angle approximation is not valid.
Angular splitting of the Sodium doublet:
Consider the two closely spaced spectral (yellow) lines of sodium (Na), 1 = 589 nm and 2 = 589.6 nm. If light from a sodium lamp fully illuminates a diffraction grating with 4000 slits/cm, what is the angular separation of these two lines in the second-order (m=2) spectrum?
Hint: First find the slit spacing d from the number of slits per centimeter.
Solution

## Slide 24: Diffraction Gratings (1)
Diffraction gratings rely on N-slit interference. They consist of a large number of evenly spaced parallel slits.
An important question:
How effective are diffraction gratings at resolving light of different wavelengths (i.e. separating closely-spaced ‘spectral lines’)?
IN = N2I1
0 /d sin 
0 2/d sin 


sin depends on .
Example: Na has a spectrum with two yellow “lines” very close together: 1 = 589.0 nm, 2 = 589.6 nm ( = 0.6 nm)
Are these two lines distinguishable using a particular grating? We need a “resolution criterion”.
Notes: 74 Xmas tree (sodium only)

## Slide 25: Diffraction Gratings (2)
We use Rayleigh’s criterion: The minimum wavelength separation we can resolve occurs when the 2 peak coincides with the first zero of the 1 peak:
So, the Raleigh criterion is (sin)min = /Nd.
However, the location of the peak is sin = m/d.
Thus, ()min = (d/m)(sin)min = /mN:
Comments:  It pays to use a grating that has a large number of lines, N. However, one must illuminate them all to get this benefit.
 It also pays to work at higher order (larger m): The widths of the peaks don’t depend on m, but they are farther apart at large m.
sin
d
d
0 /d 2/d 3/d sin 
First order Second order Third order m = 1 m = 2 m = 3

## Slide 26
Supplementary Slides

## Slide 27: Multi-Slit Interference
We already saw (slide 4) that the positions of the principal maxima are independent of the number of slits. Here, we will use phasors to determine the intensity as a function of .
At each principal maximum (d sin = m), the slits are all in phase, and the phasor diagram looks like this:
A1

A1

A1
Atot
Atot = N A1  Itot = N2 I1
A1
A1
A1
For other values of , the phasors are rotated, each by an angle  with respect to its neighbors. Remember that /2 = / = d/ sin. We can calculate Atot geometrically (next slide).
S3
S2
P
Incident wave
(wavelength )
y
L
d
S1




## Slide 28: Multi-Slit Interference (2)
The intensity for N equally spaced slits is found from phasor analysis.
Draw normal lines bisecting the phasors. They intersect, defining R as shown:

N
Atot
R
A1
R
N slits:
A1/2


R
R
Substitute

## Slide 29: Single-slit Diffraction
To analyze diffraction, we treat it as interference of light from many sources (i.e., the Huygens wavelets that originate from each point in the slit opening).
Model the single slit as M point sources with spacing between the sources of a/M. We will let M go to infinity on the next slide.
The phase difference  between first and last source is given by /2a/ = a sin /   a/ .
Destructive interference occurs when the polygon is closed ( = 2):
a
A1 (1 slit)
Aa (1 source)
P
Screen (far away)
a = a sin  a

a
L >> a implies rays are parallel.
L
Destructive Interference

## Slide 30: Single-slit Diffraction (2)
We have turned the single-slit problem into the M-slit problem that we already solved in this lecture.
However, as we let M  , the problem becomes much simpler because the polygon becomes the arc of a circle.
The radius of the circle is determined by the relation between angle and arc length:  = Ao/R.
You can graph this function
I = A2:
Remember: a = (a sin)/  a 
 = angle between 1st and last phasor
Ao
A1

R
Trigonometry: A1/2 = R sin(/2)
With R = Ao/: