## Slide 1: Profiling gem5 Simulator
Johnson Umeike, Neel Patel, Alex Manley, Amin Mamandipoor, Heechul Yun, Mohammad Alian
Architecture Research Group

## Slide 2: Executive Summary
Motivation: software-based architectural simulation is slow!
Observation: gem5 runs up to 3× faster on an M1 MacBook vs. a Xeon Dell server!
Goal: to accelerate current gem5 simulations
Approach:
  Extensively profile gem5 to identify bottlenecks
  Using performance counters & FireSim!
Results:
  gem5 is extremely front-end bound with sensitivity to L1 cache sizes
  Larger iCache and dCaches can improve simulation time be up to 68%
  Proposed system solutions to accelerate gem5
Notes: We are in the golden age of computer architecture where the continuation of Moore’s Law is premised upon the specialization of hardware for different applications. That is, computer architects are going to design more hardware. Furthermore, this involves extensive design space exploration which implies the use of software-based simulation.

## Slide 3: Outline
Introduction
Methodology
Profiling gem5 Extensively on M1 and Xeon Platforms
  Microarchitectural exploration on Xeon using Intel VTune
  Reading microarchitectural counters on M1 Platforms
Sensitivity Analysis of gem5 Simulation Speed
  Sensitivity to system configurations
  Sensitivity to architectural configurations (Running gem5 on FireSim)
Conclusion

## Slide 4: Outline
Introduction
Methodology
Profiling gem5 Extensively on M1 and Xeon Platforms
  Microarchitectural exploration on Xeon using Intel VTune
  Reading microarchitectural counters on M1 Platforms
Sensitivity Analysis of gem5 Simulation Speed
  Sensitivity to system configurations
  Sensitivity to architectural configurations (Running gem5 on FireSim)
Conclusion

## Slide 5: Exciting Observation!
gem5 ALWAYS runs significantly faster on Apple MacBook PC compared to a high-end Intel Xeon Dell server!
Collect measurement after executing PARSEC workloads on gem5.
Apple M1 with 8 phy cores
& 8GB of mem
Intel Xeon Gold with 20 phy cores
& 96GB of mem
VS
run multiple gem5 instances
run multiple gem5 instances

## Slide 6: Exciting Observation!
gem5 ALWAYS runs significantly faster on Apple MacBook PC compared to a high-end Intel Xeon Dell server!
Collect measurement after executing PARSEC workloads on gem5.
Apple M1 with 8 phy cores
& 8GB of mem
Intel Xeon Gold with 20 phy cores
& 96GB of mem
VS
run multiple gem5 instances
run multiple gem5 instances
As a result, we see up to 3.02x speedup of gem5 running on Apple MacBook PC vs. an Intel Dell Server.

## Slide 7: Research Questions?
Why does gem5 run faster on M1?
Where are the bottlenecks in running gem5 simulation?
How much faster can gem5 run by tuning micro-architecture and system configurations?

## Slide 8: How can we answer these questions?

## Slide 9: Outline
Introduction
Methodology
Profiling gem5 Extensively on M1 and Xeon Platforms
  Microarchitectural exploration on Xeon using Intel VTune
  Reading microarchitectural counters on M1 Platforms
Sensitivity Analysis of gem5 Simulation Speed
  Sensitivity to system configurations
  Sensitivity to architectural configurations (Running gem5 on FireSim)
Conclusion

## Slide 10: How to Answer These Questions?
gem5
Profiling gem5 code
  Top-Down methodology on Intel Xeon
  Performance counters on both platforms
We compare gem5 profile w/ SPEC applications
Sensitivity analysis to Micro-architectural and system-level parameters
Evaluate gem5’s performance on FireSim to validate results
Host Server Running gem5 natively
Simulated System
Host Server Running SPEC natively
SPEC 2017 Benchmark
PARSEC Benchmark
VS

## Slide 11: Host Server Configuration
Parameters | Dell Server (Xeon Gold 6242 R) | Apple MacBook (M1 Chip)
Max Frequency | 3.1 GHz (4.1 Turbo Boost) | 3.2 GHz (P) + 2GHz (E)
Cores | 20C/40T | 4C/4T (P) + 4C/4T (E)
Cacheline | 64B | 128B
iCache, dCache | 32KB, 32KB | 192KB, 128KB (P) + 128KB, 64KB (E)
L2, L3 | 20MB, 35.75MB | 12MB (P) + 4MB (E), 8MB
VM page size | 4KB | 16KB
DRAM, Total BW | 96GB DDR4-2933, 141 GB/sec | 8GB LPDDR4X-4266, 68GB/sec

## Slide 12: Host Server Configuration
Parameters | Dell Server (Xeon Gold 6242 R) | Apple MacBook (M1 Chip)
Max Frequency | 3.1 GHz (4.1 Turbo Boost) | 3.2 GHz (P) + 2GHz (E)
Cores | 20C/40T | 4C/4T (P) + 4C/4T (E)
Cacheline | 64B | 128B
iCache, dCache | 32KB, 32KB | 192KB, 128KB (P) + 128KB, 64KB (E)
L2, L3 | 20MB, 35.75MB | 12MB (P) + 4MB (E), 8MB
VM page size | 4KB | 16KB
DRAM, Total BW | 96GB DDR4-2933, 141 GB/sec | 8GB LPDDR4X-4266, 68GB/sec
M1 has 6x larger iCache and 4x larger dCache
Notes: We also measure the performance of gem5 on an Apple Mac Studio

## Slide 13: Outline
Introduction
Methodology
Profiling gem5 Extensively on M1 and Xeon Platforms
  Microarchitectural exploration on Xeon using Intel VTune
  Reading microarchitectural counters on M1 Platforms
Sensitivity Analysis of gem5 Simulation Speed
  Sensitivity to system configurations
  Sensitivity to architectural configurations (Running gem5 on FireSim)
Conclusion

## Slide 14: Profiling gem5 on Intel Xeon Processor
Use Top-Down analysis to profile gem5 and SPEC on a Xeon Cascade Lake CPU
Retiring Cycles
Cycles where CPU performs useful work
01
02
03
04
Frontend Bound
Stalled cycles while waiting for the frontend to supply ops
Backend Bound
CPU is stalled because of unavailable resources at the backend
Bad Speculation
Lost cycles due to mispredictions and bad speculations

## Slide 15: Breakdown of gem5’s Bottleneck on Intel Xeon
Chart: Fraction of CPU Bound Cycles
| geomean of representative SPEC apps | geomean across diff. gem5 configs
Retiring | 0.5048 | 0.55813
Frontend Bound | 0.21238 | 0.38559
Bad Speculation | 0.13628 | 0.035524
Backend Bound | 0.14653 | 0.020754
Retiring
Frontend
Bound
Frontend
Bound
Retiring
Backend
Bound
Bad Speculation

## Slide 16: Breakdown of gem5’s Bottleneck on Intel Xeon
Chart: Fraction of CPU Bound Cycles
| geomean of representative SPEC apps | geomean across diff. gem5 configs
Retiring | 0.5048 | 0.55813
Frontend Bound | 0.21238 | 0.38559
Bad Speculation | 0.13628 | 0.035524
Backend Bound | 0.14653 | 0.020754
Retiring
Frontend
Bound
Frontend
Bound
Retiring
Backend
Bound
Bad Speculation

## Slide 17: Now, let’s zoom into gem5’s frontend bound cycles!

## Slide 18: Breakdown of Frontend Bound Cycles
Chart: Fraction of CPU Bound Cycles
| geomean of representative SPEC apps | geomean across diff. gem5 configs
FrontEnd Latency | 0.067626 | 0.094925
FrontEnd Bandwidth | 0.034749 | 0.09129
Frontend
Latency
Frontend
Bandwidth
Frontend
Latency
Frontend
Bandwidth

## Slide 19: Breakdown of Frontend Bound Cycles
Chart: Fraction of CPU Bound Cycles
| geomean of representative SPEC apps | geomean across diff. gem5 configs
FrontEnd Latency | 0.067626 | 0.094925
FrontEnd Bandwidth | 0.034749 | 0.09129
Frontend
Latency
Frontend
Bandwidth
Frontend
Latency
Frontend
Bandwidth

## Slide 20: gem5 suffers from huge iTLB overhead and iCache misses resulting in frontend latency cycle stalls!

## Slide 21: Zoom into gem5’s Frontend Latency Bound Cycles
Chart: Fraction of CPU Bound Cycles
| geomean of representative SPEC apps | geomean across diff. gem5 configs
iCache Misses | 0.00026307 | 0.012399
iTLB Overhead | 0.00017886 | 0.041651
Branch Resteers | 0.0056516 | 0.02173
iTLB
Overhead
Branch
Resteers
iCache
Misses

## Slide 22: Zoom into gem5’s Frontend Latency Bound Cycles
Chart: Fraction of CPU Bound Cycles
| geomean of representative SPEC apps | geomean across diff. gem5 configs
iCache Misses | 0.00026307 | 0.012399
iTLB Overhead | 0.00017886 | 0.041651
Branch Resteers | 0.0056516 | 0.02173
iTLB
Overhead
Branch
Resteers
iCache
Misses

## Slide 23: Profiling gem5 on Apple M1 Processor
We measure the microarchitectural properties of this ARM-based processor from a privileged level when running gem5 and SPEC
  M1 allows a privileged user to read hardware performance counters
  We modify the simulation loop in gem5 to implement this functionality
  Then we extensively profile gem5 on the performance and efficiency cores.

## Slide 24: Some striking differences between M1 and Xeon profiles running gem5!

## Slide 25: Differences in dTLB Miss Rate
Chart: dTLB Miss Rate
M1_Pro | 0.0058412
Intel_Xeon | 0.035758
0.58%
3.58%
Xeon
M1

## Slide 26: Differences in iTLB Miss Rate
Chart: iTLB Miss Rate
MacBook | 0.0009
Intel_Xeon | 0.0069
0.09%
0.69%
M1
Xeon
M1 Page Size | Xeon Page Size
16KB | 4KB

## Slide 27: Differences in iCache Miss Rate
Chart: iCache Miss Rate
M1_Pro | 9.6716e-06
Intel_Xeon | 0.10299
0.001%
10.30%
Xeon
M1
M1 iCache Size | Xeon iCache Size
192KB | 32KB

## Slide 28: Differences in dCache Miss Rate
Chart: dCache Miss Rate
M1_Pro | 0.0009
Intel_Xeon | 0.0093
0.09%
0.93%
Xeon
M1
M1 dCache Size | Xeon dCache Size
128KB | 32KB

## Slide 29: Differences in Branch Misprediction Rate
Chart: Branch Misprediction Rate
M1_Pro | 0.14
Intel_Xeon | 0.22
0.14%
0.22%
Xeon
M1

## Slide 30: Differences in Branch Misprediction Rate
M1
Chart: Branch Misprediction Rate
M1_Pro | 0.14
Intel_Xeon | 0.22
0.14%
0.22%
Xeon
36%
Better branch predictor performance
Improvement in iTLB miss rate
Reduction in dCache misses on M1
7.7×
13.4×

## Slide 31: Outline
Introduction
Methodology
Profiling gem5 Extensively on M1 and Xeon Platforms
  Microarchitectural exploration on Xeon using Intel VTune
  Reading microarchitectural counters on M1 Platforms
Sensitivity Analysis of gem5 Simulation Speed
  Sensitivity to system configurations
  Sensitivity to architectural configurations (Running gem5 on FireSim)
Conclusion

## Slide 32: How does gem5 perform under varying system-level configurations?

## Slide 33: Sensitivity of gem5 to Huge Pages!
Chart: Execution Time in Seconds
w/o Huge Page Opt. | 7688.08
w/ Huge Page Opt. | 7300.09
w/o Huge page
w/ Huge Page

## Slide 34: Sensitivity of gem5 to Huge Pages!
Chart: Execution Time in Seconds
w/o Huge Page Opt. | 7688.08
w/ Huge Page Opt. | 7300.09
w/o Huge page
w/ Huge Page
The result of this optimization is a 63% reduction in iTLB overhead and 7% improvement in the number of retiring cycles
Many more fascinating results in our paper!

## Slide 35: So far, we have seen that Xeon is more frontend bound compared to M1. But what is the culprit?

## Slide 36: Theoretical Speculations
What are the possible reasons for gem5’s speedup on M1 platform:
  Clock speed – 3.1GHz (Xeon) vs 3.2GHz (M1)
  Cache size – 192KB L1 (Xeon) vs 32KB L1 (M1)
  Instruction Set Architecture – ARM (Xeon) vs x86 (M1)
  Number of cores – 20 cores (Xeon) vs 8 cores (M1)
  Pipelining – Maybe

## Slide 37: Theoretical Speculations
What are the possible reasons for gem5’s speedup on M1 platform:
  Clock speed – 3.1GHz (Xeon) vs 3.2GHz (M1)
  Cache size – 192KB L1 (Xeon) vs 32KB L1 (M1)
  Instruction Set Architecture – ARM (Xeon) vs x86 (M1)
  Number of cores – 20 cores (Xeon) vs 8 cores (M1)
  Pipelining – Maybe
What are the possible reasons for gem5’s speedup on M1 platform:
  Clock speed –
  Cache size –
  Instruction Set Architecture –
  Number of cores –
  Pipelining –
How can we prove this? – Modify hardware configuration

## Slide 38: Theoretical Speculations
What are the possible reasons for gem5’s speedup on M1 platform:
  Clock speed – 3.1GHz (Xeon) vs 3.2GHz (M1)
  Cache size – 192KB L1 (Xeon) vs 32KB L1 (M1)
  Instruction Set Architecture – ARM (Xeon) vs x86 (M1)
  Number of cores – 20 cores (Xeon) vs 8 cores (M1)
  Pipelining – Maybe
What are the possible reasons for gem5’s speedup on M1 platform:
  Clock speed –
  Cache size –
  Instruction Set Architecture –
  Number of cores –
  Pipelining –
How can we prove this? – Modify hardware configuration
What are the possible reasons for gem5’s speedup on M1 platform:
  Clock speed –
  Cache size –
  Instruction Set Architecture –
  Number of cores –
  Pipelining –
How can we prove this? – Modify hardware configuration
  Run gem5 on gem5? –

## Slide 39: Theoretical Speculations
What are the possible reasons for gem5’s speedup on M1 platform:
  Clock speed – 3.1GHz (Xeon) vs 3.2GHz (M1)
  Cache size – 192KB L1 (Xeon) vs 32KB L1 (M1)
  Instruction Set Architecture – ARM (Xeon) vs x86 (M1)
  Number of cores – 20 cores (Xeon) vs 8 cores (M1)
  Pipelining – Maybe
What are the possible reasons for gem5’s speedup on M1 platform:
  Clock speed –
  Cache size –
  Instruction Set Architecture –
  Number of cores –
  Pipelining –
How can we prove this? – Modify hardware configuration
What are the possible reasons for gem5’s speedup on M1 platform:
  Clock speed –
  Cache size –
  Instruction Set Architecture –
  Number of cores –
  Pipelining –
How can we prove this? – Modify hardware configuration
  Run gem5 on gem5? –
What are the possible reasons for gem5’s speedup on M1 platform:
  Clock speed –
  Cache size –
  Instruction Set Architecture –
  Number of cores –
  Pipelining –
How can we prove this? – Modify hardware configuration
  Run gem5 on gem5? –
  Run gem5 on FireSim –

## Slide 40: Simulated System on FireSim
quad-core Rocket Chip with an 8KB 2-way set associative icache & dcache, and a 512KB L2 cache base config
Parameter | Value
Design | Rocket Chip
Number of Cores | 4
L1 Instruction Cache Size | 8KB
L1 Data Cache Size | 8KB
L2 Cache Size | 512KB
Cache Block Size | 64B
Number of Sets | 64
gem5
FireSim Running gem5 as an App
Simulated System
Benchmark
FireSim on AWS F1 Instance

## Slide 41: Sensitivity of Simulation Speed to L1 Size
Chart: Simulation Time Improvement
(16KB/4 : 16KB/4 : 512KB/8) | 0.24731
(32KB/8 : 32KB/8 : 512KB/8) | 0.54736
(64KB/16 : 64KB/16 : 512KB/8) | 0.68179
16K L1
32K L1
64K L1

## Slide 42: Outline
Introduction
Methodology
Profiling gem5 Extensively on M1 and Xeon Platforms
  Microarchitectural exploration on Xeon using Intel VTune
  Reading microarchitectural counters on M1 Platforms
Sensitivity Analysis of gem5 Simulation Speed
  Sensitivity to system configurations
  Sensitivity to architectural configurations (Running gem5 on FireSim)
Conclusion

## Slide 43: Summary
gem5 is frontend bound because of its large instruction footprint
Our detailed Top-Down analysis of gem5 reveals two main bottlenecks in gem5’s execution:
  high iTLB and L1 miss rates
  high branch resteer overheads
Using FireSim we showed that:
  The size of the iCache and dCache significantly impacts gem5’s performance
Future direction is to consider the architecture of a specialized core for accelerating software-based simulators.

## Slide 44: Thank You!
For more information visit KU Architecture Research Group at
https://arg.ku.edu

## Slide 45: Backup Slides

## Slide 46: Profiling Apple M1 Processor
We measure the microarchitectural properties of this ARM-based processor from a privileged level when running gem5 and SPEC.
NB: offset-bits + index-bits <= page offset
VIPT = 2offset-bits x 2index-bits x associativity
With 192KB iCache and 128KB dCache: associativity is 12 & 8
iTLB
VIPT L1 Cache
Main Memory
VPN
Page offset
Virtual Address
Index-bits
offset-bits
miss
page table walk
VPN
Index-bits
return cache line
hit
L2-L3 Caches
miss
return PPN

## Slide 47: Discussion of Future Work
Chart: Number of Functions
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
Atomic | 0.10743 | 0.16333 | 0.20349 | 0.24327 | 0.26689 | 0.28688 | 0.30678 | 0.32242 | 0.33752 | 0.3524 | 0.36652 | 0.37818 | 0.38975 | 0.4006 | 0.41088 | 0.42101 | 0.43034 | 0.43956 | 0.44799 | 0.4564 | 0.46433 | 0.47221 | 0.47988 | 0.48656 | 0.49318 | 0.49975 | 0.50624 | 0.51265 | 0.51898 | 0.52529 | 0.53155 | 0.53746 | 0.54311 | 0.54872 | 0.55431 | 0.55984 | 0.56536 | 0.57085 | 0.57628 | 0.58147 | 0.58665 | 0.59182 | 0.59692 | 0.60176 | 0.60656 | 0.61091 | 0.61526 | 0.61953 | 0.62377 | 0.628 | 0.628
Timing | 0.090988 | 0.14212 | 0.18031 | 0.21547 | 0.24184 | 0.26129 | 0.27568 | 0.28973 | 0.30347 | 0.31681 | 0.33014 | 0.3421 | 0.35394 | 0.36446 | 0.37432 | 0.38416 | 0.39374 | 0.40224 | 0.41041 | 0.41828 | 0.42592 | 0.43337 | 0.4406 | 0.4476 | 0.45457 | 0.46148 | 0.46828 | 0.47479 | 0.48127 | 0.48774 | 0.49401 | 0.49992 | 0.50571 | 0.51148 | 0.51712 | 0.52274 | 0.52834 | 0.53372 | 0.53905 | 0.54437 | 0.54965 | 0.55493 | 0.56017 | 0.56533 | 0.57046 | 0.57544 | 0.58037 | 0.58528 | 0.59017 | 0.59502 | 0.59502
Minor | 0.029481 | 0.05357 | 0.076525 | 0.098467 | 0.11859 | 0.13733 | 0.15531 | 0.17195 | 0.18847 | 0.20373 | 0.21772 | 0.22941 | 0.23949 | 0.249 | 0.25847 | 0.26753 | 0.27651 | 0.28426 | 0.29108 | 0.29791 | 0.30418 | 0.31044 | 0.31668 | 0.32287 | 0.3287 | 0.3344 | 0.34002 | 0.34532 | 0.3505 | 0.35557 | 0.36058 | 0.36506 | 0.36953 | 0.374 | 0.37845 | 0.38288 | 0.3873 | 0.3917 | 0.39607 | 0.40042 | 0.40469 | 0.40896 | 0.41321 | 0.41746 | 0.42154 | 0.42553 | 0.42952 | 0.43346 | 0.43728 | 0.44109 | 0.44109
O3 | 0.043532 | 0.078508 | 0.10178 | 0.12435 | 0.13791 | 0.14921 | 0.16046 | 0.17001 | 0.17927 | 0.18839 | 0.19652 | 0.20326 | 0.20992 | 0.21629 | 0.22236 | 0.22821 | 0.23401 | 0.23968 | 0.24533 | 0.25055 | 0.25559 | 0.26052 | 0.26536 | 0.27019 | 0.2749 | 0.27961 | 0.28431 | 0.28898 | 0.29357 | 0.29815 | 0.30268 | 0.30705 | 0.31137 | 0.31567 | 0.31997 | 0.32405 | 0.32805 | 0.33204 | 0.336 | 0.33996 | 0.34388 | 0.34768 | 0.35144 | 0.35518 | 0.35889 | 0.36249 | 0.36605 | 0.36959 | 0.37307 | 0.37651 | 0.37651

## Slide 48: Sensitivity of gem5 to Huge Pages!
Chart: Execution Time Speedup
| gem5 O3 CPU
w/o Huge Page Opt. | 0.04
w/ Huge Page Opt. | 0.0505
W/ Huge Page
W/O Huge Page

## Slide 49: Sensitivity of gem5 to Huge Pages!
Chart: Execution Time Speedup
| gem5 O3 CPU
EHP | 0.04
THP | 0.0505
The result of this optimization is a 63% reduction in iTLB overhead and 7% improvement in the number of retiring cycles
Please see our paper for more results!

## Slide 50: Sensitivity of Simulation Speed to L1 Size
Chart: Simulation Time Improvement
| gem5 Timing CPU
(64KB/4 : 16KB/16 : 512KB/8) | 0.46285
(16KB/4 : 64KB/16 : 512KB/8) | 0.46001
(16KB/4 : 16KB/4 : 1024KB/8) | 0.22462
(16KB/4 : 16KB/4 : 2048KB/8) | 0.2456
(16KB/4 : 16KB/4 : 512KB/8) | 0.24731
(32KB/8 : 32KB/8 : 512KB/8) | 0.54736
(64KB/16 : 64KB/16 : 512KB/8) | 0.68179
iCache
dCache
L2 Cache
iCache & dCache
16K L1
32K L1
64K L1